## Slide 1: WF on NR PUCCH demodulation requirements
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#86bis
Melbourne, Australia, April 16th – 20th 2018
Agenda: 7.11.2.2
R4-1805083
Document for: Approval

## Slide 2: Test scope and performance metric
Performance requirements should be defined for all NR PUCCH formats with single-user tests.
HARQ-ACK and CSI are used as the payload for NR PUCCH performance tests. For HARQ-ACK, the performance metric is “DTX to ACK” and “missed ACK”. For CSI, the performance metric is “BLER” and “false alarm rate”.

## Slide 3: PUCCH general parameters
NR PUCCH performance requirements are defined
  For 1Tx
  With frequency hopping enabled
  For some but not all the supported cell BWs in 38.104
  SCS of 15kHz and 30kHz

## Slide 4: PUCCH format specific parameters
Format | Payload | Symbol length | PRB number
0 | 1-bit HARQ-ACK | 1, 2 | 1
1 | 2-bit HARQ-ACK | two lengths to be selected | 1
2 | 4-bit HARQ-ACK | 1, 2 | 1
3, 4 | 16-bit CSI with CSI-1 and CSI-2 | two lengths to be selected | FFS

## Slide 5: Simulation assumptions
Parameter | Value |  | Remarks
Number of Tx | 1 |  | no transparent Tx diversity considered
Number of Rx | 2, 4, 8 |  | number of diversity branches in baseband
SCS (kHz) | 15, 30 |  | 
Cell BW (MHz) | 15kHz SCS: 5, 10, 20 30kHz SCS: 10, 20, 100 |  | part of the supported BWs are tested
Carrier frequency (GHz) | 4 |  | 
Propagation channel | AWGN, TDL-C (RMS 300ns, UE speed 30km/h) |  | 
Payload size | format 0 | 1 | 
 | format 1 | 2 | 
 | format 2 | 4 | 
 | format 3/4 | 16 | with both CSI-1 and CSI-2
Symbol length | format 0 | 1, 2 | 
 | format 1 | FFS | to be down-selected from 4 to 14
 | format 2 | 1, 2 | 
 | format 3/4 | FFS | to be down-selected from 4 to 14
PRB number | format 0-2 | 1 | 
 | format 3/4 | FFS | 
Modulation | pi/2-BPSK and QPSK |  | apply for format 3/4