## Slide 1: WF on NR PUSCH demodulation requirements
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#86bis
Melbourne, Australia, April 16th – 20th 2018
Agenda: 7.11.2.2
R4-1805085
Document for: Approval

## Slide 2: Test scope and performance metric
RAN4 should focus on the basic PUSCH performance in fading channels for BS demodulation requirements.
The performance metric is the SNR for the 70% throughput of the specified FRCs.

## Slide 3: PUSCH configurations for the performance tests
PUSCH performance requirements are only defined for CP-OFDM waveform.
PUSCH performance requirements are only defined for codebook based transmission scheme with 1Tx and 2Tx.
  For 2Tx, requirements are defined for both 1-layer and 2-layer transmission.
RS
  PTRS and SRS are not modeled in the PUSCH performance tests.
  For DMRS, the performance requirements are only defined for type 1 without additional DMRS.
PUSCH performance requirements are defined for both types of time domain resource allocation.
  symbol lengths to be tested for RA type A: FFS
  symbol lengths to be tested for RA type B: FFS

## Slide 4: FRC for PUSCH performance tests
SCS
  15kHz, 30kHz
PUSCH with full cell BW allocation
  15kHz SCS: 5, 10, 15, 20MHz
  30kHz SCS: 10, 20, 40, 80, 100MHz
Modulation orders and code rate
  QPSK: FFS
  16QAM: FFS
  64QAM: FFS
  256QAM: FFS

## Slide 5: Other parameters for PUSCH performance tests
Code block group based PUSCH is disabled
Frequency hopping is disabled
Limited buffer rate matching is disabled
Number of HARQ retransmissions is 4

## Slide 6: Simulation assumptions
Parameter | Value | Remarks
Transform precoding | Disabled | only CP-OFDM is tested
Transmission scheme | Codebook based | 
Number of Tx | 1, 2 | no transparent Tx diversity considered
Number of Rx | 2, 4, 8 | number of diversity branches in baseband
Number of layers | 1 and 2 | 
DMRS type | type-1 | 
Number of DMRS symbols | 1 | no additional DMRS
Time domain resource allocation type | A, B | 
PUSCH symbol length | RA type A: FFS RA type B: FFS | down-selection needed
SCS (kHz) | 15, 30 | 
PUSCH BW (MHz) | 15kHz SCS: 5, 10, 15, 20 30kHz SCS: 10, 20, 40, 80, 100 | part of the supported BWs are tested
MCS | QPSK: FFS 16QAM: FFS 64QAM: FFS 256QAM: FFS | down-selection needed
Carrier frequency (GHz) | 4 | 
Propagation channel | AWGN, TDL-C (RMS 300ns, UE speed 30km/h) |