## Slide 1: Way forward on RRM requirements for R15 V2X CA
Huawei, HiSilicon, Qualcomm, CATT
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, Australia, 16th – 20th April, 2018
Agenda item: 6.16.3
R4-1805485

## Slide 2: Agreements on V2X Carrier Aggregation
V2X Synchronization Reference Source selection/reselection requirements for V2X sidelink CA
  When the UE does not have any sync source and have to search for syncref UE on all configured carriers: Drop rate of [TBD] data Tx, [TBD] data Rx, [TBD] SLSS Tx and [TBD] delay requirements.
    The above requirement bases on the assumption that there is only 1 SLSS sync search bloc
  When the UE have synced to one SyncRef UE in a carrier, and continue searching for other SyncRef UEs in that carrier, the existing R14 requirement for delay and Tx dropping rate applies to all carriers. The existing R14 requirement for Rx dropping applies to the searching carrier.

## Slide 3: Agreements on V2X Carrier Aggregation
Interruption requirements for V2X CC addition/release based on dedicated RRC signaling in sidelink transmission mode 3.
  No need to introduce the requirements of interruptions to V2X sidelink communication due to V2X CC addition or release.
  Upon receiving V2X carrier addition/release command by the RRCConnectionReconfiguration message that includes sl-V2X-ConfigDedicated in subframe n, the interruption to WAN of up to 2 ms is allowed no later than in downlink subframe n+22.
Delay requirements for V2X CC addition/release based on dedicated RRC signaling in sidelink transmission mode 3
  Upon receiving V2X carrier addition command by the RRCConnectionReconfiguration message that includes sl-V2X-ConfigDedicated in subframe n, one transmission of PSCCH/PSSCH on the added V2X carrier shall not be earlier than in downlink subframe n + 22.