## Slide 1: 3GPP TSG-RAN WG4 Meeting #86Bis Melbourne, Australia, 16 - 20 Mar 2018
Huawei, Ericsson
Way forward on BS FeNB-IoT demodulation performance
R4-1805490

## Slide 2: FeNB-IoT FDD part
  Early data transmission in Msg3
    No performance requirements need to be defined
  NPRACH cell range enhancements
    New performance requirements need to be introduced to verify the new numerology of 1.25kHz subcarrier spacing and 800us CP length
  Support for physical layer SR
    No performance requirements need to be defined for SR sending w or w/o HARQ ACK/NACK

## Slide 3: FeNB-IoT TDD
  NPRACH
    New performance requirements need to be defined to verify new NPRACH formats, details FFS
  NPUSCH format 1 and format 2
    Same test configurations and demodulation performance requirements as FDD can be reused as did for other BS demodulation requirements
    Set uplink-downlink configuration 1