## Slide 1: Way Forward on the Number of Beams and Cells for SSB-Based Measurements
Ericsson, Nokia, Nokia Shanghai Bell, CATT, ZTE,
NTT DoCoMo, AT&T, CMCC
3GPP TSG-RAN WG4 Meeting #86bis R4-1805499
Melbourne, Australia, 16th - 20th April, 2018
Agenda Item: 7.9.2.2

## Slide 2: Background
Agreements from RAN4#86bis:
FR1 |  |  |  | FR2 |  |  | 
Intra-frequency |  | Inter-frequency |  | Intra-frequency |  | Inter-frequency | 
# cells | # beams | # cells | # beams | # cells | # beams | # cells | # beams
8 | [12, 16] Minimum # of beam for PCell/PSCell cell should be specified (e.g. for PCell/PSCell, it can be defined as no smaller than RLM-RS resources). It is FFS for SCell. | 4 | [6, 8] |  |  | 4 | [8,12]

## Slide 3: FR1
Number of beams
  [16] beams per intra-frequency, and
    On the serving cells, the UE shall be able to measure on at least N beams, where N is the number of configured RLM-RS resources for this cell
  [8] beams per inter-frequency

## Slide 4: FR2
Number of cells
  [8] intra-frequency cells
Number of beams
  [24] beams per intra-frequency, and
    On the serving cell, the UE shall be able to measure on at least N beams, where N is the number of configured RLM-RS resources for this cell
  [12] beams per inter-frequency

## Slide 5: Summary of Proposals
Proposals are in turquoise
FR1 |  |  |  | FR2 |  |  | 
Intra-frequency |  | Inter-frequency |  | Intra-frequency |  | Inter-frequency | 
# cells | # beams | # cells | # beams | # cells | # beams | # cells | # beams
8 | 16 Minimum # of beam for PCell/PSCell cell should be specified. For PCell/PSCell: it shall be not smaller than #RLM-RS resources. | 4 | 8 | 8 | 24 | 4 | 12

## Slide 6
Annex: Summary of Companies’ Proposals before RAN4#86bis
Company | FR1 |  |  |  | FR2 |  |  | 
 | Intra-frequency |  | Inter-frequency |  | Intra-frequency |  | Inter-frequency | 
 | # cells | # SSBs | # cells | # SSBs | # cells | # SSBs | # cells | # SSBs
NTT DoCoMo |  | 14-18 |  | 7-9 | At least 7-8 | At least 18-22 |  | At least 9-11
Ericsson |  | 16 |  | 8 | 8 | 24 |  | 12
ZTE |  | 16 |  | 8 | 8 | 24 |  | 12
Nokia, Nokia Shanghai Bell |  | 16 |  | 8 | ≥6 | ≥24 |  | ≥10
Huawei, HiSilicon |  | 16 |  | 9 | 7 | 19 |  | 12
CATT |  | 16 |  | 8 | 8 | 20 |  | 12
Qualcomm |  | 12 |  | 6 | 4 | 16 |  | 8
MediaTek |  | 12 |  | 6 | 4 | 16 |  | 8
LGE |  | 12 |  | 6 | 4 | 16 |  | 8
Intel |  | 12 |  | 6 | 4 | 16 |  | 8
Samsung |  | 12 |  | 6 | 4 | 16 |  | 8