## Slide 1: Way forward on UE CSI for FeCOMP
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16 April – 20 April 2018
Agenda Item: 6.22.2
R4-1805504

## Slide 2: CSI Reporting Requirements
Previous agreements
  Antenna configuration: 2x2 ULA Low antenna correlation (for TP1-UE and TP2-UE links)
  Test setup includes 2 TPs (serving TP1 and TP2)
    No time/frequency offset between the TPs
    Colliding CRS patterns with Different Cell IDs
  CSI-RS configuration
    UE is configured with K = 2 NZP CSI-RS resources and one CSI-IM resource
    2 CSI-RS antenna ports are configured for each NZP CSI-RS resource
    ZP CSI-RS configurations are aligned among TPs
  CSI reporting assumptions:
    Aperiodic CSI reporting
    Fixed RI and CQI per TP (fixed reference channel): Rank 1, 16QAM, MCS 13
    Follow PMI and CRI
      Proposal
  Power imbalance between TP1 and TP2 is equal to [6,9] dB
  Codebook subset restriction per NZP CSI-RS resource: 001111
  TDD mode: UL/DL configuration 2 and special subframe type 4

## Slide 3: CSI Reporting Requirements
      Test metrics
  Test metric #1:
    is the throughput obtained at SNR1 using the CRI configured according to the CSI UE report
    is the throughput obtained at SNR1 under assumption of single TP1 transmission
    Purpose: Verify that CRI2 reporting provides performance improvement over CRI 0,1 reporting
  Test metric #2:
    CRI2 reporting probability: For SNR1 CRI2 shall be reported more than αCRI2 % of the time.
    αCRI2 = FFS
    Purpose: Verify that CRI2 is correctly reported in the high SNR range
  Test metric #3:
    CRI0 reporting probability: For SNR2 CRI0 shall be reported more than αCRI0 % of the time.
    αCRI0 = FFS
    Purpose: Verify that CRI0 is correctly reported in the low SNR range
      Test points
  SNR1 corresponds to [70, 90]% of the maximum throughput using the CRI configured according to the CSI UE report
  SNR2 corresponds to [70, 90]% of the maximum throughput under assumption of single TP1 transmission