## Slide 1: Way forward on beam management
Ericsson
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16 – 20 April, 2018
R4-1805530

## Slide 2: Background
For beam management RAN4 will specify the requirements of
  1) L1-RSRP reporting and
  2) Beam failure and recovery
    Requirements are based on both SSB based, CSI-RS based and SSB and CSI-RS based.
L1-RSRP reporting
  Part of CSI reporting
  Cover periodic, aperiodic, or semi-persistent reporting
Beam failure recovery consists of:
  Beam failure detection, and
  Beam identification
  Reference: 38.213 Section 6
    For threshold for beam failure, Q_outLR, RAN1 assumption is hypothetical PDCCH BLER of 10%.

## Slide 3: Way forward on beam failure recovery (BFR)
FFS to clarify the definition of beam failure and whether to introduce the beam failure detection requirements in RAN4.
Companies are encouraged to investigate:
  Evaluation period for beam link failure detection with/without DRX
    SSB-based and CSI-RS based and CSI-RS+SSB based
  Whether it is feasible to reuse RLM out-of-synch framework or new sets of parameter values are needed
    PDCCH configuration parameters
  UE is not assumed to perform BFR outside its active DL BWP
FFS whether and how to define the new beam identification requirements.

## Slide 4: Way forward on L1-RSRP reporting
Companies are encouraged to investigate whether measurement period of L1-RSRP needs to be specified and whether this will be part of core requirements or performance part.
L1-RSRP measurement accuracy shall be performance part.
FFS whether L1-RSRP core and performance requirements will be specified in TS38.133 or in TS 38.101-4.