## Slide 1: 3GPP TSG-RAN WG4 Meeting #86Bis Melbourne, Australia, 16 - 20 Mar 2018
Huawei, Nokia, Nokia Shanghai Bell, Ericsson
Way forward on NR BS demodulation performance
R4-1805538

## Slide 2: Test Methodology
  FR1
    Conducted
      Same as LTE conducted requirements definition methods
    OTA
      Reuse eAAS demodulation test framework unless technical issues are identified, and pending on completion of eAAS
  FR2
    OTA: Default baseline as in FR1 unless any technical issues identified

## Slide 3: General
Define the following NR BS performance requirements in Rel-15
  PUSCH
  PUCCH
  PRACH
Single user is baseline
  Single carrier is baseline

## Slide 4: General open issues in Test Configuration
Propagation Condition
  Option1: Consider to use the conclusions from UE demod discussions, if feasible
  Option 2: consider the BS demod independently from UE discussion
Duplex mode
TDD UL DL configuration
  Consider only semi-statically configured UL DL configurations
Antenna configuration
BW
SCS
Reference receiver
  only noise is modeled in the tests (no explicit interferer modeled) in Rel-15
Consider how to capture CA, EN-DC and SUL based on single carrier cases
Study multiple user test cases after single user tests cases are completed, if needed

## Slide 5: Performance Requirements
PUSCH
  No UCI multiplexing on PUSCH
  Test metric: 70% maximum throughput
  FFS: Waveform
  FFS: DMRS configuration
  FFS: FRC
PUCCH
  Format
    Whether all formats or a subset of the all formats are tested
  Test metric
    For HARQ-ACK: DTX to ACK, and missed ACK, other metrics not precluded
    For CSI, if introduced: BLER
    FFS which metric is used for which formats
PRACH
  Preamble Format
    Whether all formats or a subset of them are tested
  FFS: whether type of restricted sets are to be tested
  FFS: Test metric

## Slide 6: Annex - Reference
R4-1803743 Preliminary views on NR BS demodulation requirements for FR1, China Telecom
R4-1804619 On BS demodulation requirements for NR, Ericsson
R4-1805081 On general issues for NR BS demodulation requirements, Nokia, Nokia Shanghai Bell
R4-1805082 Initial discussion on BS demodulation requirements for NR PUCCH, Nokia, Nokia Shanghai Bell
R4-1805083 WF on NR PUCCH demodulation requirements, Nokia, Nokia Shanghai Bell
R4-1805084 Initial discussion on BS demodulation requirements for NR PUSCH , Nokia, Nokia Shanghai Bell
R4-1805085 WF on NR PUSCH demodulation requirements , Nokia, Nokia Shanghai Bell
R4-1805110 Initial discussion on BS demodulation requirements for NR PRACH , Nokia, Nokia Shanghai Bell
R4-1805111 WF on NR PRACH demodulation requirements , Nokia, Nokia Shanghai Bell
R4-1805313 Discussion on NR BS FR1 demodulation performance requirements, Huawei
R4-1805314 Discussion on NR BS FR2 demodulation performance requirements, Huawei