## Slide 1: 3GPP TSG-RAN WG4 Meeting #86Bis Melbourne, Australia, 16 - 20 Mar 2018
Huawei, HiSilicon, …
Way forward on 8Rx demodulation requirements
R4-1805552

## Slide 2: PDSCH demodulation performance tests
  TM2
    Rank 1, 16QAM 1/2, EVA5, 2x8 medium correlation B
  TM3
    Rank 2, 16QAM 1/2, EVA70, 2x8 low
  FFS
    Applicability rule of CRS-based demodulation and SDR test for a UE that supports 8Rx processing only in case the UE is configured with transmission modes supporting more than 4 layers.
    Whether to introduce rank 5~8 demodulation performance tests
    Whether to differentiate 8Rx UE and 8-layer UE

## Slide 3: SDR tests
  64QAM
    Rank: 8
    Tx EVM: 6%
    MCS
      Option 1: MCS 22
      Option 2: MCS 23
      Other options are not precluded
  256QAM
    Rank: FFS
    Tx EVM: 3%
  FFS: rank 2/4 SDR tests
    Option 1: reuse legacy tests by applicability rule
    Option 2: define new test cases