## Slide 1: 3GPP TSG-RAN WG4 Meeting #86Bis Melbourne, Australia, 16 - 20 Mar 2018
Huawei, Ericsson, Qualcomm
Way forward on sTTI DMRS pattern and CQI2MCS mapping table
R4-1805560

## Slide 2: General
Use sTTI pattern [2 3 2 2 2 3] during the test for performance requirements.
Set different MCS which leads to the code rate nearest to the target coding rate for different slot/subslot TTI
RAN4 sets 4x2 with low correlation for CRS-based PDSCH demodulation requirements with sTTI.
For DMRS-based TM9 sPDSCH transmission, non-MBSFN shall be configured
Company is welcome to check if any issues based on the current simulation assumptions considering the different coding rate between the initial transmission in sTTI with 3OS and retransmission in sTTI with 2OS.
Company is welcome to check the CQI2MCS mapping table in slide 5 and 6.

## Slide 3: DMRS pattern- 1
Subslot-TTI
  vshift = 0 for all sTTI
  DMRS is transmitted in subslot #1, #3, and #5

## Slide 4: DMRS pattern- 2
Slot-TTI
  vshift = 0 for slot#0 and slot#1

## Slide 5: CQI2MCS mapping Table
Use the following CQI2MCS table to evaluate the subband CQI reporting with PUSCH 3-1
CQI Index |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | Notes
Target Coding Rate |  |  | OOR | 0.0762 | 0.1172 | 0.1885 | 0.3008 | 0.4385 | 0.5879 | 0.3691 | 0.4785 | 0.6016 | 0.4551 | 0.5537 | 0.6504 | 0.7539 | 0.8525 | 0.9258 | 
Modulation |  |  | OOR | QPSK |  |  |  |  |  | 16QAM |  |  | 64QAM |  |  |  |  |  | 
MCS Scheme | PRB | Available RE-s | Imcs |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MCS.sTTI_1 | 12 | 792 | DTX | 0 | 0 | 2 | 4 | 6 | 9 | 12 | 14 | 16 | 19 | 21 | 23 | 26 | 27 | 27 | Slot TTI CRS-based
MCS.sTTI_2 | 12 | 264 | DTX | 0 | 0 | 1 | 4 | 6 | 8 | 11 | 13 | 16 | 19 | 21 | 23 | 25 | 27 | 27 | Subslot TTI CRS-based
MCS.sTTI_3 | 12 | 756 | DTX | 0 | 0 | 2 | 4 | 6 | 8 | 11 | 13 | 16 | 18 | 21 | 23 | 25 | 27 | 27 | Slot TTI DMRS-based non-CSI-RS
MCS.sTTI_4 | 12 | 252 | DTX | 0 | 0 | 1 | 3 | 6 | 8 | 11 | 13 | 15 | 18 | 20 | 22 | 25 | 27 | 27 | Sub-slot TTI DMRS-based non-CSI-RS
Note 1: Mapping between Imcs and TBS according to Tables 7.1.7.1-1 and 7.1.7.2.1-1 in TS 36.213 [6]. Note 2: 2 symbols allocated to PDCCH. Note 3: Subslot or slot TTI in sub-frame#0 and #5 are not used for the corresponding requirement except for [MCS.23]. The next subframe (i.e. sub-frame#1 or #6) shall be used for potential retransmissions. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 6: CQI2MCS mapping Table
Use the following CQI2MCS table to evaluate the wideband CQI reporting with PUSCH 1-1
CQI Index |  |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | Notes
Target Coding Rate |  |  | OOR | 0.0762 | 0.1172 | 0.1885 | 0.3008 | 0.4385 | 0.5879 | 0.3691 | 0.4785 | 0.6016 | 0.4551 | 0.5537 | 0.6504 | 0.7539 | 0.8525 | 0.9258 | 
Modulation |  |  | OOR | QPSK |  |  |  |  |  | 16QAM |  |  | 64QAM |  |  |  |  |  | 
MCS Scheme | PRB | Available RE-s | Imcs |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MCS.sTTI_5 | 50 | 3300 | DTX | 0 | 0 | 2 | 4 | 7 | 9 | 12 | 15 | 16 | 19 | 21 | 23 | 26 | 27 | 27 | Slot TTI CRS-based
MCS.sTTI_6 | 50 | 1100 | DTX | 0 | 0 | 2 | 4 | 6 | 9 | 12 | 15 | 16 | 19 | 21 | 23 | 25 | 27 | 27 | Subslot TTI CRS-based
MCS.sTTI_7 | 50 | 3150 | DTX | 0 | 0 | 2 | 4 | 6 | 8 | 11 | 15 | 16 | 18 | 21 | 23 | 25 | 27 | 27 | Slot TTI DMRS-based non-CSI-RS
MCS.sTTI_8 | 50 | 1050 | DTX | 0 | 0 | 2 | 4 | 6 | 8 | 11 | 15 | 16 | 18 | 20 | 23 | 25 | 27 | 27 | Sub-slot TTI DMRS-based non-CSI-RS
Note 1: Mapping between Imcs and TBS according to Tables 7.1.7.1-1 and 7.1.7.2.1-1 in TS 36.213 [6]. Note 2: 2 symbols allocated to PDCCH. Note 3: Subslot or slot TTI in sub-frame#0 and #5 are not used for the corresponding requirement except for [MCS.23]. The next subframe (i.e. sub-frame#1 or #6) shall be used for potential retransmissions. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 7: Simulation assumption
Refer to R4-1805495