## Slide 1: Observations on Sync Raster with “small shift”
Intel,
3GPP TSG-RAN WG4 Meeting #86bis R4-1805676
Melbourne, AU, 16 -22 April, 2018

## Slide 2: Basic design criteria for sync raster
At least one SSB should be fully contained within the minimum channel BW (i.e. 4.5MHz@15kHz SCS or 8.64MHz@30kHz SCS) with aligned RE boundary
To meet this criterion,
  When SCS=15kHz, for each channel raster point, there is at least one sync raster point, of which the corresponding distance to the channel raster point is no more than 450kHz and is divisible by 15kHz
  When SCS=30kHz, for each channel raster point, there is at least one sync raster point, of which the corresponding distance to the channel raster point is no more than 720kHz and is divisible by 30kHz

## Slide 3: Illustration of basic design criteria for sync raster

## Slide 4: Issue with existing “short shift” designs
Alternative 1: N*900kHz+M*5kHz ; Alternative 2: N*700kHz+M*5kHz
Without loss of generality, channel raster point 1000kHz, 900kHz are considered to check if the basic design criteria can be fulfilled
  In the following table, all sync raster points within 450kHz and 720kHz from the channel raster points for 15kHz and 30kHz SCS respectively are included
  Sync raster points are highlighted in red if the corresponding distance is divisible by SCS
  No sync raster points satisfy the basic criteria in the boxes highlighted in orange.
  Observation: for existing alternatives with “short shift”, none of them can meet the basic design criteria.
 |  | Alternative 1 | Alternative 2
Channel raster point=1000kHz | SCS=15kHz | 895kHz, 900kHz, 905kHz | 695kHz, 700kHz, 705kHz, 1395kHz, 1400kHz, 1405kHz
 | SCS=30kHz | 895kHz, 900kHz, 905kHz | 695kHz, 700kHz, 705kHz, 1395kHz, 1400kHz, 1405kHz
Channel raster point=900kHz | SCS=15kHz | 895kHz, 900kHz, 905kHz | 695kHz, 700kHz, 705kHz, 1395kHz, 1400kHz, 1405kHz
 | SCS=30kHz | 895kHz, 900kHz, 905kHz | 695kHz, 700kHz, 705kHz, 1395kHz, 1400kHz, 1405kHz