## Slide 1: WF on SCS restrictions of BWP based on CC BW
Qualcomm
3GPP TSG-RAN WG4 RAN#86 Bis
Melbourne, Australia, April 16th- 20th, 2018
R4-1805678
Document for: Approval

## Slide 2: Background
In RAN4 AH-1801 the following agreements were reached [1]
  UE behavior
    The UE meets RF requirements related to it’s configured BWP according to UE CBW (no additional BWP related RF requirements)
      FFS whether UE CBW next highest value after BWP bandwidth
    How the UE configures it’s RF in order to operate the BWP and meet the CBW based RF requirements is implementation dependent
  In addition the UE has the following options when configured with BWP smaller than CC BW
    UE behavior: BWP configured w/ smaller PRBs compared to UE CC BW
    Option1: Do not change the UE operating CC BW even if the configured BWP is less than UE configured CC BW
    Option2: Changed the UE operating CC BW according to the new allocated BWP

## Slide 3: Example of restriction on SCS of BWP based in UE CC BW
Consider a UE configured with a CC BW of 100MHz with 30KHz SCS and a BWP of 50MHz, 15KHz
  Based on option 1 in previous agree the UE should be able to keep operating in 100MHz RF BW
  This would imply using a 4K point FFT in baseband
  However, the BWP of 50MHz , 15KHz alone would need a 4K point FFT
  Thus, in order to keep operating with 100MHz RF BW to meet the RF requirements and extract only a 50MHz component when in BWP (50MHz, 15Khz SCS), the UE would need to do a 8K point FFT which would be beyond its capabilities.
The above implies that when a UE is configured to CC BW of 100MHz with 30KHz SCS, it cannot have a BWP of 50MHz with 15 KHz SCS.
SCS of BWP need to be restricted based on configured UE CC BW so that the UE can operate its RF in CC BW
  The restriction will be that FFT size based on BWP SCS and UE CC BW should not exceed UE capability.

## Slide 4: Agreements and Proposal
Agreement: How the UE configures it’s RF in order to operate the BWP and meet the CBW based RF requirements is implementation dependent
Proposal: SCS for a BWP needs to be restricted such that the FFT size needed for a UE operating in CC BW with BWP SCS will not exceed UE capabilities.

## Slide 5: References
[1] R4-1801006, WF on wideband operation of NR UE, 3GPP TSG-RAN WG4 #AH-1801 Meeting, San Diego, California, USA, Jan. 22 – 26, 2018