## Slide 1: WF on beam correspondence test methodology at FR2
LG Electronics, Qualcomm Incorporated, MediaTek
3GPP TSG-RAN WG4 #86BIS Meeting Melbourne, Australia, 16 - 20 April 2018 Agenda Item: 7.4.8.12
R4-1805703

## Slide 2: Background
RAN4 discussed how to define the beam correspondence RF requirements in TS38.101-2.
Interested companies provided the detail test methodology and some clarifications as below
  [1] LGE (R4-1803984): Further evaluation for beam correspondence RF requirements
  [2] MediaTek (R4-1804336): FR2 UE beam correspondence requirement
  [3] Qualcomm (R4-1804661): Definition of UE beam correspondence requirement for FR
  [4] Intel (R4-1804160): Beam correspondence for FR2
  [5] Sony (R4-1805322): On UE Beam Correspondence and EIS spherical coverage
During online/offline discussions, companies discussed the principle of beam correspondence RF requirements and pros and cons according to the proposed test methodologies.
UE is able to determine a UE Tx beam for the uplink transmission based on UE’s downlink measurement on UE’s one or more Rx beams
In RAN1 feature lists, they captured with yellow highlight as “the beam correspondence is mandate at least FR2”, but it is still discuss on RAN1.

## Slide 3: Summary of comparison
Test method | Pros | Cons
[3] by Qualcomm | - Align the beam correspondence definition - For test time aspect, It will be required middle level test time | - No EIRP CDF test time saving for UEs with beam correspondence capability as UL beam sweeping is always required. - Not possible guarantee the beam correspondence when consider wider or isotropic beam at UE
[1] by LGE | - Align the beam correspondence definition - Evaluate difference of direction and power between Tx and Rx beam | - Not simple test compare with MTK proposal - Need to know UE ant. Configuration and adjust the antenna position
[2] by MTK | - UE implicitly verify by using the spherical coverage test | - Can not differentiate “full” and “partial” beam correspondence

## Slide 4: WF on Basic principle
1. Satisfy the Beam correspondence Definition:
  UE aspects in RAN1:
    UE is able to determine a UE Tx beam for the uplink transmission based on UE’s downlink measurement on UE’s one or more Rx beams.
    UE is able to determine a UE Rx beam for the downlink reception based on TRP’s indication based on uplink measurement on UE’s one or more Tx beams.
2. On top of the first condition, the metric to choose the test methodology for beam correspondence is test simplicity to save the OTA test time

## Slide 5: Agreements
Beam correspondence requirement should be only based on UE Tx EIRP measurements performed by the TE.
Beam correspondence requirements definition will be further discussed based on the following two approaches, [other approaches not precluded]:
  1st approach: define the beam correspondence requirement based on an EIRP tolerance between the best Tx beam and the Tx beam selected based on DL measurements.
  2nd approach : define the beam correspondence requirement based on EIRP CDF requirements. In this case, the correspondence is defined based on passing the EIRP CDF requirements without UL Tx beam sweeping.
  Companies provide their preferred approach at next RAN4 meeting
RAN4 will define a beam correspondence requirement based on bullets 1, 2
RAN4 will decide if beam correspondence RF requirement can be tested simultaneously with other Tx requirements.
  * Whether it is mandatory or not for beam correspondence is up to decision of RAN1 and RAN

## Slide 6: Informative only
The following definition was proposed for 1st approach [3]
  The beam correspondence requirement measures the ability of the UE to select a corresponding beam for UL transmission based on DL measurements. A corresponding beam is defined as follows:
  For any link direction between UE and BS, the UE selected beam for UL transmission is a “corresponding beam” if the UE EIRP measured for the selected beam is within X dB from the maximum achievable EIRP in the same direction. X dB is the beam correspondence tolerance.
  To declare beam correspondence the UE shall be able to select a corresponding beam in any link direction.