## Slide 1: WF on NR A-MPR evaluation scenarios for n50, n51, and n74
NTT DOCOMO, INC., Huawei, Etisalat
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16 - 20 Apr 2018
R4-1805727

## Slide 2: Background
In the RAN4 #85-AH1801 meeting, MPR values were already discussed.
A-MPR evaluation scenarios was provided in R4-1804545.
There are requests in online session to correct a wrong simulation value e.g channel bandwidth cases, to make A-MPR evaluation scenario more clear by including n50 and n51.

## Slide 3: Way forward
Below is proposals in original paper:
Proposal 1: The frequency range of FDD band of 43MHz should be used for NR system in 1430-1470 MHz and used for narrow band systems in 1427-1430 MHz to utilize frequency resources while meeting the EESS protection.
Proposal 2: A-MPR evaluation for n74 to protect EESS should be conducted for each CBW of 5 MHz, 10 MHz, 15 MHz, and 20 MHz at the frequency offset of 3 MHz from the lower band edge of 1427 MHz by the next meeting RAN4#87.
Proposal 3: A-MPR evaluation for n74 to protect own Rx should be conducted based on the same scenarios as B74 in TR 36.751[1] by the next meeting RAN4#87.
  The simulation assumptions are 25 28dB IQ image and LO suppression, 60 dB CIM3 suppression, and PA calibration point so that ACLR is just met with full QPSK allocation (worst of UTRA1, UTRA2, and E-UTRA), for each channel bandwidth separately.
Proposal 4: As with LTE, A-MPR evaluation for MSS protection is unnecessary because FDD UL transmission is apart from the frequency band of MSS.
Proposal 5: As with LTE, A-MPR evaluation for Band 11 protection should be conducted with the transmission frequency of 1447.9-1462.9 MHz and CBW of 10 MHz and 15 MHz.

## Slide 4: Way forward
A-MPR evaluation for n50, n51, and n74 is conducted as shown in below table
Note 1: The unwanted emission power level is to be understood here as the level measured with the mobile station transmitting at an average output power of 15 dBm.
Lband (1427-1518MHz): A-MPR studies for UE |  |  |  | 
Proposals 1 | Summary of the A-MPR study to protect EESS and MSS for the bands n50, n51 & n74 and to protect Band 11 for n74 |  |  | 
 | Band | n74 | n50 | n51
 | EESS protection level | -32dBm/27MHz1 in the 1400-1427MHz | -32dBm/27MHz1 in the 1400-1427MHz | -32dBm/27MHz1 in the 1400-1427MHz
 | MSS protection level | No need | -0.8dBm/MHz EIRP in 1518-1520MHz + -30dBm/MHz EIRP in 1520-1559MHz | No need
 | Band 11 protection level | The requirements specified in Table 6.2.4-1 of TS36.101(NS_09) in the Rx 1475.9-1510.9MHz | No need | No need
 | Own Rx protection | The requirements specified in Table 6.2.4-29 of TS36.101(NS_39) in the Rx 1475-1488MHz | No need | No need
Proposals 2 | Definition of the studies: |  | Tx CBW [MHz] | Protected Band [MHz]
 | n74 [MHz] => Study the Tx only in the 1440-1470MHz band to protect Rx 1475-1488MHz band |  | 10, 15, 20 | 1475-1488
 | n74 [MHz] => Study the Tx only in the 1447.9-1462.9 MHz band to protect Rx 1475.9-1510.9 MHz band |  | 10, 15 | 1475.9-1510.9
 | n74 [MHz] => Study the Tx only in the 1430-1470MHz band to protect EESS which is in 1400-1427MHz band |  | 5, 10, 15, 20 | 1400-1427
 | n50 [MHz] => Study the Tx only in the 1432-1517MHz band to protect EESS which is in 1400-1427MHz band |  | 5, 10, 15, 20, 40, 50, 60 | 1400-1427
 | n50 [MHz] => Study the Tx only in the 1432-1517MHz band to protect MSS which is in 1518-1559MHz band |  | 5, 10, 15, 20, 40, 50, 60 | 1518-1559
 | n51 [MHz] => Study the Tx only in the 1427-1432MHz band to protect EESS which is in 1400-1427MHz band |  | 5 | 1400-1427