## Slide 1: WF for UE RF AH specific for DC_(n)71B
Nokia, TMO, Skyworks, Qualcomm, Intel, LGE, Ericsson
R4-1805761

## Slide 2: WF 1/4
Following agreements were reached in AH [1]
Use single PA and single antenna UE architecture in A-MPR studies for DC_(n)71B
Use equal PSD in A-MPR studies for LTE and NR.
  Study for un-equal PSD is not precluded
Define two sets of A-MRP. One A-MPR(1) for case that LTE and NR modems know each other’s allocation and another A-MPR(2) for the case that LTE and NR modems do not know each other’s allocation.
Use A-MPR versioning to indicate which A-MPR UE supports is an option that can be discussed.

## Slide 3: WF 2/4
A-MPR is used to address following emission requriements
    Spectrum emission mask, current or the one proposed in [10], dependes on decision in RAN4#86bis
    ACLR, (use new ACLR definition R4-1805461)
    Protection of bands 12 and 29
    requirement is -50 dBm/1 MHz for bands 12 and -38 dBm/1MHz for band 29.
    filter rejection to band 12 is at least 25 dB [9]
    filter rejection to band 29 is at least 10 dB [9]
Self-desentization is specified with MSD and no A-MPR is used to mitigate MSD

## Slide 4: WF 3/4
• A-MPR(1) for case that LTE and NR modems know each other’s allocation equal power reduction to LTE and NR is applied.
• A-MPR(2) for case that LTE and NR modems do not know each other’s allocation power reduction scheme is such that worst case assumption should be taken as a function of the allocation in the carrier under test.
• A-MPR(1) for case that LTE and NR modems know each other’s allocation LTE like allocation ratio is used to define A-MPR(1) .
• A-MPR(1) allocation ratio definition can be used also for A-MPR(2) but the allowed A-MPR is read from allocation curve differently.

## Slide 5: WF 4/4
There will be non-contiguous MSD defined.
Companies to provide proposals to next meeting on non-contiguous MSD test points and requirement

## Slide 6: References
[1] R4-1805740, AH minutes for UE RF AH specific for DC_(n)71B, Nokia
[9] R4-1802243, Measurements of power backoff requirements for DC_(n)71B with single PA, Qualcomm Incorporated
[10] R4-1804260, Power back-off and RX desense for intra-band EN-DC, Ericsson