## Slide 1: WF for RF requirements for Coherent UL MIMO
Qualcomm, []
R4-180xxxx
3GPP TSG-RAN WG4 Meeting #86
Melbourne, Aus, 16-20 Apr, 2018
Agenda item: 7.4.6.10 [FR1] Coherent UL MIMO

## Slide 2: Background
RF requirements for coherent UL MIMO have been discussed for the past few meeting in RAN4.
The goal has been to define a spec for phase and power error drift from the last SRS transmitted over a time window.
Some of the documents discussed in RAN4 are:
  R4-1805109, UE RF Requirements for ULMIMO, 3GPP TSG-RAN4 #86, Melbourne, Aus, 16-20 Apr, 2018
  R4-1802327, Coherent UL MIMO: UE Spec Limits on Gain and Phase Imbalance, 3GPP TSG-RAN4 #86, Athens, GR, 26 Feb – 2 Mar, 2018.

## Slide 3: Way Forward
For UL MIMO, relative power and phase difference between the two chains is of importance.
Power and phase error shall be measured as:
  A relative delta between the power and phase difference between the two chains computed at the last SRS and at any other time after that within the time window specified.
The goal of the requirement is to ensure that UE can maintain a power and phase error within a bound for a period of time after every SRS transmitted.

## Slide 4: Way Forward
Proposed spec for phase error, power error and the time window is shown below.
Phase error | Power error | Time window
¦ error ¦ ≤ [40] degrees | ¦ error ¦ ≤ [4] dB | [20] msec
Time window starts after the last symbol in which SRS is sent.
  This time window is independent of SCS
The above requirements only apply to:
  FR1
  The UEs that signal capability for “Coherent UL MIMO”
  The antennas that are in coherence at any given time.

## Slide 5: Way Forward
For the purposes of test :
  SRS RB configuration shall be the same as the of the data
  SRS shall be sounded in the same slot and same symbol on both the antennas
  Single SRS with the same RB configuration of that of data shall be sent on both the chains at the same time.

## Slide 6: Way Forward
Conditions under which these requirements do not need to be met:
  If within that 20 msec window from the last SRS, UL MIMO is disabled
    In this case at least one of the Tx chains is disabled.
    So when the UL MIMO is re-enabled within that 20 msec and Tx chain is re-enabled, then phase error of the PLL cannot be bounded.
But if the UL MIMO is active for the entire window:
  The phase error spec still applies during all UL slots within the window.