## Slide 1: WF on FR1 HPUE behavior
CMCC
3GPP TSG-RAN WG4 Meeting #86bis R4-1805776 Melbourne, AU, 16th – 20th April, 2018

## Slide 2: Background
The TDD UL/DL configuration problem was raised in RAN4#AH 1801 and way forwards were approved in R4-1801125 and R4-1802714

## Slide 3: Way Forward
To solve the SAR issue for power class 2 UE, a UE capability of maxUplinkDutyCycle is proposed to be defined which represents the maximum percentage of uplink time that can be scheduled during [X]ms to ensure compliance with applicable electromagnetic energy absorption requirements.
  The default value of maxUplinkDutyCycle is 50%. E.g. If the field is absent, the UE shall apply the default value.
For a power class 2 capable UE operating on Band n41 n77 n78 n79, when the percentage of uplink time scheduled by the network in [X]ms is larger than its capability, the requirements for power class 2 are not applicable, and the corresponding requirements for a power class 3 UE shall apply.
Notes: ----- 会议笔记(18/4/23 15:07) -----
1. 行业终端SAR测试如何执行？
2. 直播，网联无人机，上行需求大

## Slide 4: Way Forward
Send a LS to inform RAN2 on the signaling impact.
RAN4 continue to discuss and determine the value of evaluation period [X]ms in May meeting

## Slide 5: Reference
[1] R4-1804016 Discussion on solutions to satisfy SAR requirements for NR HPUE
[2] R4-1804074 Discussion on NR FR1 HPUE behaviour
[3] R4-1803659 Further discussion on UL/DL configurations for NR HPUE