## Slide 1: WF on NR BS EVM window length
Nokia, Nokia Shanghai Bell, Huawei, …
R4-1805801
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16-20 April 2018
Agenda Item: 7.6.2.4.1.1

## Slide 2: Background (1/)
During RAN4#86bis meeting BS EVM window length was discussed in the following contributions:
  [1] R4-1804986 EVM Window for NR, Ericsson
  [2] R4-1803937 BS EVM window length, Huawei, HiSilicon
  [3] R4-1804460 Further discussion on EVM window length, ZTE Corporation
  [4] R4-1804955 Further discussion on NR BS EVM window length, Nokia, Nokia Shanghai Bell
This document summarizes the way forward on BS EVM window length

## Slide 3: Background (2/3)
In E-UTRA specifications EVM window length is the same for BS and UE.
During RAN4 AH-1801 meeting following agreement for UE EVM window length was agreed:
    Window length ‘W’ used in EVM calculation shall be [3.5]% of FFT length for various numerologies.

## Slide 4: Background (3/4)
For FR1:
  Based on [1-4] following 2 options for BS EVM were proposed:
    Option 1: The window length W for EVM measurements is defined as 3.5% of FFT size which correspond to 50% of CP length for all CBW
    Option 2: The window length W for EVM measurements is defined as:
    2.8% of FFT size which correspond to 40% of CP length for CBW up to 25 MHz
    4.4% to 6.0% of FFT size which correspond to 62.5% to 85% of CP length for CBW above 25 MHz
  Option 1 proposes to adopt in EVM calculation single value in % of FFT length.
  Option 2 proposes to adopt in EVM calculation different values in % of FFT length for different channel bandwidths.

## Slide 5: Background (4/4)
For FR2:
  Based on contributions submited before and in [1-4] following option for BS EVM were proposed:
    Option 1: The window length W for EVM measurements is defined as 3.5% of FFT size which correspond to 50% of CP length for all CBW

## Slide 6: Agreements (2/2)
For FR1:
  It is proposed to agree conditionally on Option 1.
  If companies provide technical justyfication why Option 2 should be selected Option 2 can be further considered.
  Decision on BS EVM window length for FR1 should be taken on RAN4#87.
For FR2:
  Further discussion and decision on BS EVM window length for FR2 should be taken on RAN4#87.