## Slide 1: WF on Channel model for Demodulation for FR2
Qualcomm, Keysight Technologies, Spirent
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, Australia, 16th – 20th April, 2018
Agenda item: 7.12.4
R4-1805895

## Slide 2: Background
The WF in R4-1803560 stated
Proposal#1: Define demodulation requirements with TDL channel models
    The detailed TDL definition is FFS
    Channel models defined for FR2 in 38.901 could be a starting point
    How the models can be emulated in the tests is FFS
    Generation of TDLs from CDLs is not precluded
Proposal#2: Further study the modifications necessary to channel models to capture effect of beamforming and antenna pattern
Proposal#3: Further study the modifications necessary to simplify TDL channel models

## Slide 3: Options for channel modeling
2 options for channel models have been proposed
  Option 1. Use TDL channel models as described in 38.901
    Each tap is modeled based on the Jakes fading model
    Generation of TDLs from CDLs is not precluded based on the procedure described in TS 38.901
  Option 2. Generate TDL channel model based on the methodology in next slide
    A methodology for deriving TDLs from CDLs is provided in 38.901, however, this process does not say how to derive the Doppler spread of each tap form the CDL
    This methodology also clarifies how the Doppler spread of each tap is derived on based on which parameters
    The doppler shift of each tap will depend on the UE speed and movement direction, PAS, AoA, ZoA, ASA, ZSA

## Slide 4: Proposed TDL Generation Methodology for Option 2
The CDL framework in 38.901 is used to derive the non-spatial TDLs used for FR2 demodulation requirements
The TDL generation procedure will include spatial filtering using assumed gNB and UE antenna patterns
  gNB antenna model is FFS (one example is an 8x8 URA 0.5 λarray with 22.75 dB directivity as described in R4-1711826)
  For UE this is FFS
The Doppler spectrum for the TDL will be derived from the CDL and not assume a Jakes spectrum
  The doppler shift of each tap will depend on the UE speed and movement direction, PAS, AoA, ZoA, ASA, ZSA
For each channel model for demodulation performance testing in FR2, following parameters need to be defined:
  Base CDL channel model defined in TR 38.901
  Delay Spread
  Angular Spread for AOA, AOD, ZOA and ZOD
  Mean Angle for AOA, AOD, ZOA and ZOD.
  Alternatively, Correlation between Tx antennas in case of more than one Tx antennas

## Slide 5: Way Forward
Proposal 1: Decide on the feasible TDL channel modeling methodologies as a part of NR Testability SI. Companies are asked to provide input on whether channel emulation is feasible for the two identified candidate TDL channel modeling methodologies
Proposal 2: If both candidate methodologies are agreed to be feasible, further down-select between the two in the scope of NR UE Performance requirements work
Proposal 3: Further discuss the parameters (e.g. PDP) for the TDL channel models as a part of NR WI Performance part.