## Slide 1: Way Forward on Proposals on Concluding the SI
Intel, CATR, […]
3GPP TSG-RAN WG4 Meeting #86bis Melbourne, Australia, 16th – 20th April, 2018
Agenda item: 7.12.1
R4-1805899

## Slide 2: Background
The list of open issues from the latest status report RP-180235 is provided below:
  For UE RRM testing methodology
    Define how to model propagation conditions between the DUT and the emulated gNB sources.
    For any alternate method(s) identified, verify equivalence per agreed criteria and quantify impact on the measurement uncertainty budget.
  For UE demodulation testing methodology
    Finalize the baseline measurement setup.
    Define how to model propagation conditions between the DUT and the emulated gNB sources.
    For any alternate method(s) identified, verify equivalence per agreed criteria and quantify impact on the measurement uncertainty budget.

## Slide 3: RRM
Background: Evening AH agreements
  NMAX_AoAs:
    Baseline: NMAX_AoAs = 2
    Further study if NMAX_AoAs > 2 needed in the NR WI performance part (TR 38.810 v2.0.0 already states: For the scope of Rel-15 testing, it is assumed that NMAX_AoAs = [2]. The validity of this assumption depends on the definition of the test requirements.)
  Open items on RRM to be addressed in RAN4 #87 to decide on the applicability criteria
    QZ
    Whether RRM measurement shall be done in the far field and far field criteria
    RRM performance metrics and impact on the test methodology. Feasibility of using test methods for measurement of target RRM performance metrics.

## Slide 4: RRM
Proposals on open issues:
  NMAX_AoAs
    References related to more than 2 simultaneously active probes to be removed from the TR.
  Quiet Zone and Far field criteria
    Option 1: Leverage as much as possible the corresponding Quiet Zone characterization and Far field criteria from RF DFF method [as baseline]. Extend this analysis for 2 probe scenario with different angular offsets.
    Option 2: Evaluate the impact of measuring in any of the 3 measurement areas (Reactive NF, Radiative NF, FF).
    Other methods not precluded.
  Fading Propagation Condition:
    Channel modelling framework (i.e. methodology) adopted for Demodulation testing can be reused. Different parametrization not excluded.
  Metrics and Initial assessment of MU elements
    Identification of test metrics based on the current status of the Core Requirement (E.g. Timing accuracy, RSRP accuracy…)
    Feasibility of metric implementation.
    Initial assessment of the MU elements related to the identified metrics.

## Slide 5: Demodulation
Proposals for open items on Demodulation to be addressed in RAN4#87:
Whether the system needs to be operated in the far field is FFS
  Option 1: system operates in far field
  Option 2: system operates in near field
Whether and how to assess the Quality of the Quiet Zone is TBD.
Perform an initial assessment of MU factors of target UE Demodulation performance metrics to evaluate the feasibility of test methodology.
  Achievable SNR accuracy and SNR range

## Slide 6: Other topics
Measurement grid definition for RF scope and Channel Model definition for Demodulation have been handled in separate WFs.