## Slide 1: WF on the EIRP accuracy at extreme conditions for FR2 BS
CMCC
TSG-RAN Working Group 4 (Radio) meeting #86bis R4-1805910
Melbourne, Australia, 16th – 20th April 2018

## Slide 2
Background
R4-1802971 Output power accuracy extreme conditions Huawei
R4-1803023 BS type 2-O extreme conditions requirement for transmit power Nokia
R4-1803850 Discussion of EIRP accuracy of extreme condition of FR2 BS CMCC
R4-1804461 Discussion on FR2 EIRP accuracy under extreme temperature ZTE
So far two levels of ±3.4dB (i.e. ∆ = 0dB) and ± 4.5dB (i.e. ∆ = 1.1dB) have been proposed for for the EIRP accuracy at extreme condition for FR2 base station.
Where ∆ is the additional accuracy value based on the normal conditions (see slide 4).
For FR2 base station, the EIRP accuracy at extreme condition needs fully understand of the whole system: PA, phase shifter, antenna, radome ,testing complexity , measurement uncertainty, base band control algorithm and etc.And the deadline of Rel 15 core requirement is JUNE 2018.

## Slide 3: Way Forward
Companies are encouraged to propose the value of the EIRP accuracy at extreme condition in 3GPPRAN4#87 meeting, and get a conclusion of the value in 3GPPRAN4#87.
IF the value for this requirement can not be agreed, one of the two options shall be chosen :
  Option 1, vendor declare one additional accuracy value based on the EIRP accuracy at normal condition.(detailed in slide 4).
  Option 2, remove the requirement from REL 15 and continue discussion this requirement in REL 16.

## Slide 4: Way Forward
 | normal condition | extreme condition
Accuracy | ±3.4dB | ±(3.4dB +∆)
Range | (EIRP-3.4,EIRP+3.4) | (EIRP-3.4-∆, EIRP+3.4+∆)
EIRP is the declared EIRP level by vendor, ∆ is the additional accuracy value based on the normal conditions.