## Slide 1: WF on measurement gaps for dense PRS
Ericsson
3GPP TSG-RAN WG4 Meeting #86bis R4-1805955
Melbourne, Australia, 16th - 20th April, 2018
Agenda Item: 6.18.4.4

## Slide 2: New gaps and RSTD measurements
A new measurement gap pattern is configured for UE that requires such gaps for performing RSTD measurements configured via LPP
Impact on RSTD requirements:
  The existing UE Cat M1 and Cat M2 accuracy requirements for RSTD measurements in gaps shall also apply with the new gaps
  RAN4 to check whether the existing UE Cat M1 and Cat M2 measurement period requirements (generically formulated with respect to MGL and MGRP) for RSTD measurements in gaps also apply with the new gaps

## Slide 3: New and legacy measurement gap patterns
FFS whether legacy measurement gap patterns can be used in parallel with new gaps, choose between options:
  Option 1: using the earlier configured leagacy gaps shall be suspended during the RSTD measurement period (while new gaps are used) and resumed after the RSTD measurements are complete (when new gaps are no longer used)
  Option 2: the legacy gaps may be used during the RSTD measurement period, in parallel with new gaps (the details are FFS)
FFS gap alignment between legacy measurement gap and new RSTD measurement gap

## Slide 4: New gaps and RRM measurements
New measurement gap patterns shall not be requested if UE is not configured with RSTD measurements via LPP
FFS using the new gaps (when configured for RSTD) for RRM during the RSTD measurement period, choose between options:
  Option 1: new gaps shall not be used for RRM measurements
  Option 2: new gaps may be used for RRM measurements, under certain conditions (conditions FFS)
Impact on RRM requirements:
  RAN4 to discuss the impact of new gaps on RRM requirements, including intra-frequency and inter-frequency RRM requirements

## Slide 5: New measurement gap patterns
The new measurement gap pattern configurations are to be specified assuming X=0.15 (MGL/MGRP < X [R4-1803147])
  Other rules are not precluded