## Slide 1: Way forward on NB-IoT channel quality reporting in MSG-3
Ericsson
3GPP TSG-RAN WG4 Meeting #86bis
Melbourne, Australia, 16 – 20 April, 2018
R4-1805957

## Slide 2: Backgrounds
RAN4#86bis discussed the LS from RAN1 on NB-IoT downlink channel quality determination and report, and observed as follows:
  UE should estimate the SINR of the serving cell, where NPDCCH is transmitted, to be able to report the downlink channel quality, similar to RLM.
  SINR estimation for channel quality reporting could be based on a shorter evaluation period than RLM and using only the most recent measurement samples, e.g., NRS received during MSG2 decoding and MSG3 preparation.
  UE’s channel quality reporting in MSG3 is strictly conditioned on the successful decoding of MSG2.
  RAN2 are going to decide the number of available bits used for MSG3-based quality reporting, but it is limited (e.g., at most 2-3 bits).

## Slide 3: Way forward
Companies are encouraged to investigate the solution to report the channel quality in MSG3.
  Option 1: Based on SINR estimation from MSG2
  Option 2: Based on the combination of actual repetition used until successful decoding of MSG2 and SINR estimation from MSG2
  Other options are not precluded.
Companies are encouraged to investigate the accuracy of the SINR measurement from MSG2
  Other measurement period, e.g. before MSG1 transmission, is not precluded.

## Slide 4: Information
Timeline from MSG1 to MSG3 in the NB-IoT random access