## Slide 1: Way forward on demodulation and CSI requirements for high capacity stationary wireless link and 1024QAM
Huawei, HiSilicon, Anritsu, Rohde & Schwarz
3GPP TSG-RAN WG4 Meeting #86bis R4-1805959
Melbourne, Australia, Apr 16 – 20th, 2018
Agenda Item: 6.19.4

## Slide 2: Demodulation requirements under fading conditions
Parameters | Value
Bandwidth | 10MHz
Channel model | EPA5
CFI (OFDM symbol for control channel) | 1
Duplex mode | FDD
Table 1: common parameters
For 1024QAM demodulation requirements, the candidate test cases given in Table 2 with the common parameters given in Table 1 are identified
  The parameters of MIMO layer, MCS and Tx EVM need further study

## Slide 3: Demodulation requirements under fading conditions
Table 2: Cases for evaluation
No. | TM | PMI feedback (pre-coding) | MIMO layer | MCS | Antenna config. | Tx EVM
1 | TM4 | Wideband PMI Option 1: Feedback (PUSCH 3-1, Reporting interval =1) Option 2: Random | Op1: 1-layer Op2: 2-layer | MCS#23 (with 52752 bits) FFS: other MCS for 1-layer | 4x2 Low | Op1: 1.5% Op2: 2%
2 | TM4 | Wideband PMI Option 1: Feedback (PUSCH 3-1, Reporting interval =1) Option 2: Random | Op1: 1-layer Op2: 2-layer | MCS#23 (with 52752 bits) FFS: other MCS for 1-layer | 4x4 Low | Op1: 1.5% Op2: 2%
3 | TM9 | Wideband PMI Option 1: Feedback Option 2: Random | Op1: 1-layer Op2: 2-layer | MCS#23 (with 52752 bits) FFS: other MCS for 1-layer | 4x2 Low | Op1: 1.5% Op2: 2%
4 | TM9 | Wideband PMI Option 1: Feedback Option 2: Random | Op1: 1-layer Op2: 2-layer | MCS#23 (with 52752 bits) FFS: other MCS for 1-layer | 4x4 Low | Op1: 1.5% Op2: 2%
For 1024QAM demodulation requirements, the candidate test cases given in Table 2 with the common parameters given in Table 1 are identified

## Slide 4: Demodulation requirements under fading conditions
Further investigate and decide the parameters for 1024QAM
  To decide the parameters of MIMO layer and MCS, the simulation results corresponding to the test cases given in Table 2 in slide #2 will be provided
    SNR at 70% maximum throughput
  Target SNR range: TBD (Companies bring proposals)
  The test conditions shall ensure that max throughput can be reached for the selected MCS
  TX EVM
    Option 1: 1.5%
    Option 2: 2%
  RX EVM
    Baseline: 0%
    Other options are not precluded

## Slide 5: SDR test
Test parameters
  Target SNR range: TBD (Companies bring proposal)
  Transmission mode: TM3
  MCS: TBD
  Antenna configuration: 2 x 2 for 2-layer transmission per CC, and 4 x 4 for 4-layer transmission per CC
  CFI = 1
  Tx EVM
    The value for fading will be used for SDR test

## Slide 6: Information only: TE vendor input on Tx EVM
From TE vendors
  Anritsu and R&S state that 2% EVM was achievable in the test system, but not 1.5% EVM.
  The simulation requirement EVM becomes a requirement on the conformance test system.

## Slide 7: DMRS overhead reduction
Table 1. DM-RS table for OCC4 DM-RS support for rank 3/4 SU-MIMO transmission
DMRS ports 7,8,11,13 with OCC=4
16QAM, EPA5, 4-layer, FRC test case number TBD