## Slide 1: WF on network-based CRS interference mitigation
Ericsson
3GPP TSG-RAN WG4 Meeting #87 R4-1806567
Busan, South Korea, 21st – 25th May 2018
Agenda Item: 6.29

## Slide 2: Requirements in 36.133
For Rel-15 UE supporting network-based CRS mitigation:
  Reuse the existing RRM requirements, while clarifying the applicability conditions

## Slide 3: Scenarios and Warm-Up/Cool-Down Subframes
UE operation | Warm-up period | Full BW during: | Cool-down period
Paging | 1 | All configured paging occasions | 0
SIB1 | 1 | SIB1 transmissions | 0
SI reading | 1 | SI-windows | 0
RA | 1 | For Msg2: from the start of RAR window until Msg2 is received and DRX is configured For Msg4: see DRX Active Time | 0
 | 1 | prior to PRACH transmission (see corresponding warm up period) | N/A
eDRX | No additional warm-up subframes outside of PTW | Inside PTW: Some subframes (according to the above), otherwise 6 RBs CRS outside PTWs | No additional warm-up subframes outside of PTW
NOTE: 6 PRB CRS is needed in MBSFN subframes, except those configured as positioning subframes with PRS or belonging to the UE DRX Active Time. |  |  | 

## Slide 4: Scenarios and Warm-Up/Cool-Down Subframes (cont.)
UE operation | Warm-up | Full BW during: | Cool-down
Non-DRX operation | N/A | All subframes | N/A
DRX cycle length≤X | 1 | UE Active Time | 0
DRX/eDRX cycle length>X | TBD | UE Active Time | 0
RSTD measurements | 0 | PRS subframes | 0
RLM | N/A | When signal quality for UE is low, e.g., RS-SINR<TBD or RSRQ<TBD | N/A
MPDCCH monitoring in non-DRX | 1 | MPDCCH subframes, if no scheduled data | 0
HD-FDD | N/A | UL transmission gaps | N/A
NB-IoT | N/A | NRS subframes | N/A
Scheduling | 1 | in semi-persistently scheduled DL resources; in the resources with HARQ feedback; on-going (re)transmissions in UL/DL are covered by DRX Active Time | 0
SCell activation/deactivation of configured SCells | N/A | SCell activation period and when the SCell is activated except for the SCell deactivation period (from receiving deactivation command until it is deactivated) | N/A
SR-over-PRACH | 1 | For Msg2: From the start of RAR window until Msg2 is received For Msg4: see DRX Active Time | 0
 | 1 | prior to PRACH transmission (see corresponding warm up period) | N/A
SR-over-PUCCH | N/A | 3 ms after the subframe in which the UE sent SR on PUCCH and until UL grant has been transmitted | N/A
RA due to HO | 1 | From the start of RAR window until HO complete (RRC connection reconfiguration complete) | 0
NOTE: 6 PRB CRS in MBSFN subframes, except those configured as positioning subframes with PRS or belonging to the UE DRX Active Time. |  |  |