## Slide 1: WF on NR PUSCH demodulation requirements
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#86bis
Busan, Korea (Republic of), May 21st – 25th 2018
Agenda: 7.12.2.2
R4-1806651
Document for: Approval

## Slide 2: Test scope and performance metric
RAN4 should focus on the basic PUSCH performance in fading channels for BS demodulation requirements.

## Slide 3: PUSCH configurations for the performance tests
PUSCH requirements for CP-OFDM are defined for FR1 and FR2. Optional requirements for SC-FDM are defined for FR2.
PUSCH performance requirements are only defined for codebook based transmission scheme with 1Tx and 2Tx.
  For 2Tx, requirements are defined for both 1-layer and 2-layer transmission.
RS
  The performance requirements are only defined for DMRS type 1 without additional DMRS.
  Phase noise is not explicitly modeled in the FR2 performance requirements.
PUSCH performance requirements are defined for both types of time domain resource allocation. RAN4 needs to down-select the symbol lengths to be tested.
  symbol lengths to be tested for RA type A: FFS
  symbol lengths to be tested for RA type B: FFS

## Slide 4: FRC for PUSCH performance tests
SCS
  FR1: 15kHz, 30kHz
  FR2: 60kHz, 120kHz
PUSCH with full cell BW allocation
  15kHz SCS: 5, 10, 15, 20MHz
  30kHz SCS: 10, 20, 40, 80, 100MHz
  60kHz SCS: 50, 100, 200, 400MHz
  120kHz SCS: 50, 100, 200, 400MHz
Modulation orders and code rate
  Pi/2-BPSK (for SC-FDM only): FFS
  QPSK: FFS
  16QAM: FFS
  64QAM: FFS
  256QAM: FFS

## Slide 5: Other parameters for PUSCH performance tests
Code block group based PUSCH is disabled
Frequency hopping is disabled
Limited buffer rate matching is disabled
Number of HARQ retransmissions is 4

## Slide 6: Simulation assumptions