## Slide 1: WF on NR PUCCH demodulation requirements
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#87
Busan, Korea (Republic of), May 21st – 25th 2018
Agenda: 7.12.2.3
R4-1806653
Document for: Approval

## Slide 2: Test scope and performance metric
Performance requirements should be defined for all NR PUCCH formats with single-user tests.
HARQ-ACK and CSI are used as the payload for NR PUCCH performance tests. For HARQ-ACK, the performance metric is “DTX to ACK” and “missed ACK”. For CSI, the performance metric is “BLER” and “false alarm rate”.

## Slide 3: PUCCH general parameters
NR PUCCH performance requirements are defined
  For 1Tx
  With frequency hopping enabled
  For some but not all the supported cell BWs in 38.104
  15kHz and 30kHz SCS for FR1, and 60kHz and 120kHz SCS for FR2

## Slide 4: PUCCH format specific parameters
Format | Payload | Symbol length | PRB number
0 | 1-bit HARQ-ACK | 1, 2 | 1
1 | 2-bit HARQ-ACK | two lengths to be selected | 1
2 | 4-bit HARQ-ACK | 1, 2 | 1
3, 4 | 16-bit CSI with CSI-1 and CSI-2 | two lengths to be selected | FFS

## Slide 5: Simulation assumptions