## Slide 1: Proposed conclusion on BS requirements for LTE-NR uplink sharing
Huawei, HiSilicon, Vodafone, Orange, Intel
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea, 21-24 May, 2018
Agenda: 7.3.2
R4-187231

## Slide 2: Background
RAN4 has been discussing BS requirements for UL sharing for several meetings
At RAN4_AH-1801, it was agreed to focus on two scenarios:
  Scenario 1: LTE and NR subcarriers with same SCS (15kHz) and NR has 7.5kHz raster shift in Rel-15
    LTE and NR with different waveforms (CP-OFDM and S-OFDM) and waveform conforming technique
  Scenario 2: LTE and NR subcarriers with different SCS
    LTE and NR with different waveforms (CP-OFDM and S-OFDM) and waveform conforming technique

## Slide 3: Background
For Scenario 1, the following aspects were investigated [R4-1801568, R4-1803893]:
  Orthogonality and guard band for the cases of both perfect and realistic time and frequency synchronization between different UEs
  RX requirements with TX on
  Potential RX requirements differentiation between UL sharing from network perspective and UE perspective
Conclusion for Scenario 1:
  Orthogonality at the BS RX can be achieved and no guard is needed in the presence of 7.5kHz shift and TA. BS demodulation performance is similar to the single RAT case of either LTE or NR
  The TX to RX interference in BS receiver side has been already verified in LTE or NR and there is no further TX to RX interference for UL sharing. So no additional BS receiver verification is needed with TX on.
  No additional BS RX requirements or verifications is needed for UL sharing from network perspective, UE perspective with TDM operation and UE perspective with FDM operation.

## Slide 4: Background
For Scenario 2, the following aspects were investigated [R4-1800920]:
  Orthogonality and guard band
Conclusion for Scenario 2:
  some guard band is required
  However, it is worth noting even there is guard band required, the size of guard band can be left to implementation/deployment. This approach was adopted in 38.104 for BS supporting FDMed mixed numerologies.

## Slide 5: Proposed conclusion
It is proposed that for UL sharing from network perspective or UE perspective (both TDM and FDM operation), no additional NR BS requirements need to be introduced