## Slide 1: Way forward on CSI-RS based intra-frequency measurement requirements
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #87 Busan, Korea, 21st – 25th May, 2018
Agenda item: 7.10.13
R4-1807291

## Slide 2: Way forward on CSI-RS intra-freq measurement
RAN4 will define the measurement period TCS-RS_measurement_period of CSI-RSRP/RSRQ/SINR for CSI-RS based intra-frequency measurement with and without measurement gaps.
RAN4 study whether or when to relax the measurement period in FR2:
The requirements on measurement period can be relaxed in considering of the following aspects:
  Timing misalignment between CSI-RS resource and DRX cycle on-duration.
  Overlapping between CSI-RS resource and SMTC/SSB when different SCSs are configured.
  Overlapping between CSI-RS resource and measurement gap
  The scaling principles for SSB based measurements can be reused.

## Slide 3: Way forward on CSI-RS based measurement period
The measurement samples within one CSI-RS based measurement period is defined as in Table 1.
Table 1: TCSI-RS_measurement_period for different configurations
Configuration | Measurement bandwidth [RB] | CSI-RS resource Density | TCSI-RS_measurement_Period
0 | 24 | 1 | 20 samples
1 | 48 | 1 | 10 samples
2 | ≥96 | 1 | 5 samples
3 | ≥24 | 3 | 5 samples