## Slide 1: Way forward on NR RRC requirements
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #87 Busan, Korea, 21st – 25th May, 2018
Agenda item: 7.10.8.3
R4-1807386

## Slide 2: For NR RRC re-establishment
Proposal 1: Enhancement of TUL_grant should be done according to RAN2 agreements for NR RRC re-establishment, and TUL_grant = 0 in NR.
Proposal 2: For RRC re-establishment delay requirements, Tmargin should include impact from software processing and RF re-tuning delay.
Proposal 3: For RRC re-establishment delay requirements, Tsearch should include impact from AGC settling.
Proposal 4: For RRC re-establishment delay requirements, the exact value of Tsearch should be derived after AGC settling problem is thoroughly discussed in NR RRM requirements.

## Slide 3: For NR RRC release with redirection
Proposal 5: For NR RRC release with redirection requirement, we reuse the LTE equation as baseline.
Proposal 6: Specify NR RRC release with redirection requirements for the below scenarios at least for R15:
  Redirection to NR carriers
  Redirection to E-UTRAN TDD and FDD carriers.