## Slide 1: WF on NB-IoT downlink channel quality determination and report
Ericsson
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea (Republic of), 21 – 25 May, 2018
R4-1807938

## Slide 2: Agreements
The UE report one of N candidate values which gives a minimum supported NPDCCH repetition number to satisfy the hypothetical NPDCCH with BLER less than 1%.
  N = 3 for RRCConnectionReestablishmentRequest-NB
    Message contents: {candidateRep_1, candidateRep_2, candidateRep_3}
  N = 12 for all the messages except for RRCConnectionReestablishmentRequest-NB
    Message contents: {candidateRep_A, candidateRep_B, candidateRep_C, candidateRep_D, candidateRep_E, candidateRep_F, candidateRep_G, candidateRep_H, candidateRep_I, candidateRep_J, candidateRep_K, candidateRep_L}
  Actual values of candidate_x to be specified in RAN4 RRM specification TS36.133.

## Slide 3: Way forward
Actual values of candidate_x in MSG3
  For RRCConnectionReestablishmentRequest-NB, companies are encouraged to propose the actual values for {candidateRep_1, candidateRep_2, candidateRep_3}
    Companies are encouraged to investigate the reporting three values
  For other messages, the reported values are {1,2,4,8,16,32,64,128,256,512,1024,2048}.

## Slide 4: Way forward
From RAN4 perspective there could be two measurement periods UE can use to derive the NPDCCH repetition number to satisfy the hypothetical NPDCCH BLER of 1%:
  T1: period used for NRSRP estimation for NPRACH CE level decision
  T2: period from the beginning of MSG2 reception to the beginning of MSG3 transmission
It is up to UE implementation to use T1 and/or T2 to estimate the downlink channel quality as far as UE meets the accuracy requirement.
  Accuracy requirement is defined to report the NPDCCH repetition number to satisfy the hypothetical NPDCCH BLER of 1%
  The reporting accuracy will be verified with the corresponding test case.
RAN4 to specify the following requirements in TS36.133 core specification. FFS to how to specify.
  The measurement period
  The accuracy requirements of reported repetition numbers

## Slide 5: Information
Timeline from MSG1 to MSG3 in the NB-IoT random access