## Slide 1: WF on eFeMTC UE demodulation and CSI requirements for BL UEs
Huawei, HiSilicon, ...
3GPP TSG-RAN WG4 Meeting #87 R4-1808009 Busan, Korea (Republic of), 21 - 25 May 2018

## Slide 2: DL 64QAM
Agreement:
  CE Mode A with 3PRB allocation, TBS=968 and under EPA5 2x1 low
  Transmission mode:
    Option 1: TM6
    Option 2: TM2

## Slide 3: High velocity
Agreement:
  TM2, QPSK 1/3, (TBS=504bits with 6PRB), EPA200, 2x1 Low, CE Mode A, without frequency hopping
  Repetition:
    Option 1: No repetition
    Option 2: 8 repetitions

## Slide 4: CRS muting
Select test cases from
  Cat-M1
    8.11.1.1.1.1 Test 1 (TM6, 16QAM 1/2, 3PRB, CE Mode A, No repetitions)
    8.11.1.1.2.1 Test 1 (TM9, QPSK 1/3, 6PRB, CE Mode A, 8 repetitions)
    8.11.1.1.3.1 Tests 1 (TM2, QPSK 1/10, 6PRB, CE Mode B, 64 repetitions)
    8.11.1.1.3.1 Tests 2 (TM2, 16QAM 1/2, 3PRB, CE Mode A, No repetitions)
  Cat-M2
    8.11.1.1.3.2 Tests 1 (TM2, QPSK 1/3, 18PRB, CE Mode A, 8 repetitions)
    8.11.1.1.3.2 Tests 2 (TM2, QPSK 1/10, 18PRB, CE Mode B, 32 repetitions)
FFS number of test cases

## Slide 5: PBCH demodulation requirements
Do not introduce new requirements

## Slide 6: CQI reporting
CQI definition with the CQ table right. Test point(s) are chosen so that UE report CQI indices 11 or more for 64QAM.
CQI index | modulation | code rate x 1024 x | efficiency x
0 | out of range |  | 
1 | QPSK | 40 | 0.0781
2 | QPSK | 78 | 0.1523
3 | QPSK | 120 | 0.2344
4 | QPSK | 193 | 0.3770
5 | QPSK | 308 | 0.6016
6 | QPSK | 449 | 0.8770
7 | QPSK | 602 | 1.1758
8 | 16QAM | 378 | 1.4766
9 | 16QAM | 490 | 1.9141
10 | 16QAM | 616 | 2.4063
11 | 64QAM | 466 | 2.7305
12 | 64QAM | 567 | 3.3223
13 | 64QAM | 666 | 3.9023
14 | 64QAM | 772 | 4.5234
15 | 64QAM | 873 | 5.1152

## Slide 7: CQI reporting (Con’t)
CQI definition with the CQ table right. Test point(s) are chosen so that UE report CQI indices for QPSK or 16QAM
CQI index | modulation | code rate x 1024 | Repetition
0 | Out of range |  | 
1 | QPSK | 56 | 32
2 | QPSK | 207 | 16
3 | QPSK | 266 | 4
4 | QPSK | 195 | 2
5 | QPSK | 142 | 1
6 | QPSK | 266 | 1
7 | QPSK | 453 | 1
8 | QPSK | 637 | 1
9 | 16QAM | 423 | 1
10 | 16QAM | 557 | 1
11 | 16QAM | 696 | 1
12 | 16QAM | 845 | 1
13 | 64QAM | 651 | 1
14 | 64QAM | 780 | 1
15 | 64QAM | 888 | 1