## Slide 1: WF on NR PUSCH demodulation requirements in Rel-15
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 RAN#86bis
Busan, Korea (Republic of), May 21st – 25th 2018
Agenda: 7.12.2
R4-1808024
Document for: Approval

## Slide 2: Test setup
Transmission scheme
  Option 1: performance requirements are defined only for 1Tx transmission schemes.
  Option 2: performance requirements are defined only based on codebook-based transmission schemes
    Number of layers for 2Tx CP-OFDM based PUSCH tests
      FFS both 1 layer and 2 layers are to be tested
DMRS
  Single-symbol DMRS configuration are tested in Rel-15
    Option 1:
      only 1 front-loaded symbol;
    Option 2:
      1 front-loaded symbol + one additional DMRS symbol
    Option 3:
      only 1 front-loaded symbol, and
      1 front-loaded symbol + one additional DMRS symbol
    Option 4:
      only 1 front-loaded symbol, and
      1 front-loaded symbol + one additional DMRS symbol, and
      1 front-loaded symbol + two additional DMRS symbols
  FFS DMRS types (type 1 and type 2) are to be tested
PTRS
  Not introduced PTRS for FR1 tests.
  FFS for FR2

## Slide 3: Test setup
SRS
  Not modeled in the tests
Time domain resource allocation
  For FR1, slot based transmission is tested, FFS non-slot based transmission
  For FR2, FFS for slot-based or non-slot based transmission
  FFS resource mapping type (type A or type B)
MCS
  Selected from QPSK, 16QAM and 64QAM
  FFS pi/2-BPSK
Other
  Code block group based PUSCH is disabled in the tests
  Frequency hopping is disabled in the tests
    FFS: whether to introduce specific test case for frequency hopping
  Limited buffer rate matching is disabled in the tests
    FFS: whether to introduce specific test case for limited buffer rate matching
  Number of HARQ transmissions is 4
Testing metric
  SNR @70% of maximum throughput of the FRC
  Other metric is not precluded for some specific test cases

## Slide 4: Simulation assumptions (For alignment only)
Parameter | Value |  | Remarks
 | FR1 | FR2 | 
Transform precoding | Disabled | Disabled | 
Transmission scheme | Codebook based | Codebook based | 
Number of Tx | 1 | 1 | no transparent Tx diversity considered
Number of Rx | 2 | 2 | number of diversity branches in baseband
Number of layers | 1 | 1 | 
DMRS type | Type-1; Type-2: FFS | Type-1; Type-2: FFS | 
Number of DMRS symbols | Case 1: 1+1 (Symbol #2 and #11) Case 2: 1 front-loaded | Case 1: 1+1 (Symbol #2 and #11) Case 2: 1 front-loaded | 
Time domain resource allocation type | Type A and/or Type B | Type A and/or Type B | 
PUSCH symbol length | 14 OFDM symbols | RA Type A: [14 ] OFDM symbols RA Type B: [11] OFDM symbols | 

## Slide 5: Simulation assumptions (For alignment only)
Parameter | Value |  | Remarks
 | FR1 | FR2 | 
MCS index | QPSK: [2 or 4] 16QAM: [13 or 16] 64QAM: [25] | QPSK: [2 or 4] 16QAM: [13 or 16] 64QAM: [25] | 
Carrier frequency (GHz) | 4 | 30 | 
Propagation channel | AWGN | AWGN | 
Time offset | Not modelled | Not modelled | 
Freq_offset | Not modelled | Not Modelled |