## Slide 1: 3GPP TSG-RAN WG4 Meeting #87 Busan,Korea, May 21~May 25, 2018
Ericsson, Nokia, Nokia Shanghai Bell, Huawei, Samsung
Way forward on NR PRACH demodulation requirements
R4-1808026

## Slide 2: PRACH
Test cases are only defined for a subset of preamble PRACH formats

## Slide 3: PRACH
Test metric
  NR PRACH performance metric is the SNR for False alarm probability and Missed detection probability
  The requirements on timing estimation error should be further studied

## Slide 4: PRACH requirements
FFS: the test for Restricted sets in Rel-15
Preamble Format (For Rel-15)
  For long sequence, requirements are defined for:
    Format 0
    FFS for format 1/2/3
  For short sequence, requirements are defined for which PRACH format(s) are FFS
    No performance requirements for A2/B2, A3/B3

## Slide 5: PRACH simulation assumption
Channel condition
  AWGN channel is used for simulation alignment
    No frequency offset is considered
  Performance requirements will be defined for fading channel if no technical issues are identified, and the propagation condition to be used is FFS
NCS
  Format 0: Ncs=[13] (for simulation alignment)
  Companies are encouraged to bring more input on the Ncs configuration on the Ncs value of short sequence in the coming meetings

## Slide 6: PRACH
BW/SCS/Format combination (for simulation alignment purpose)
  Format:
    For FR1
      Format 0
      FFS: A1, A3, B1, B4, C2
    For FR2
      FFS A1, A3, B1, B4, C2, C0
  Other options are not precluded

## Slide 7: PRACH simulation
In simulation, checking the target SNR for False alarm probability < [0.1]% and Missed detection probability <[1]%