## Slide 1: WF on simulation assumptions for NR UE performance tests
Ericsson
3GPP TSG-RAN WG4 Meeting #87 Busan, South Korea, 27 Nov - 1 Dec 2017
Agenda Item: 9.4.4.1
R4-1808027

## Slide 2: Background
Based on first two rounds of adhoc discussions, the previous agreements were captured in agreed MoM R4-1807994.
There were more agreements made during the third round adhoc discussions.
All agreements for simulation assumptions agreed in this meeting RAN4#87 are captured in the following slides this way forward, in order to give guideline for next meeting for interested companies to provide simulation results for alignment purpose.

## Slide 3: Test coverage
First focused on the mandatory features
FFS for handling mandatory features with and without capability signalling in same priority or not

## Slide 4: Configurations of Channel bandwidth and SCS (Channel Bandwidth +SCS)
Introduce performance requirements in band agnostic manner per frequency range at least for FR1
Selected some combination(s) of {Channel bandwidth, SCS} as starting point for early stage simulation alignment purpose
  Candidate options for FR1:
    20MHz + 30kHz
    10MHz+ 15kHz
    40MHz +30kHz
  Candidate options for FR2:
    100 MHz + 120 kHz (baseline for alignment simulation purpose)
    100 MHz + 60 kHz
    200 MHz + 120 kHz
Additional test cases for other specific combinations can be further discussed

## Slide 5: TDD DL/UL configuration (1/2)
Introduce multiple configurations covering different scenarios (30 kHz), FFS for detailed configurations.
  FFS for other numerologies
Configuration for different SCSs will be decided separately
Test set-up
  FR1:
    15 kHz: DDDSU(aligned with LTE config#2 with 5ms periodicity)
      S = 12D+1Gp+1U

## Slide 6: TDD DL/UL configuration (2/2)
Candidate options for initial simulation alignment purpose:
  FR1 15 kHz:
    DDDSU(aligned with LTE config#2 with 5ms periodicity)
      S = 12D+1Gp+1U
  FR1 30 kHz:
    DDDSU
    7D1S2U
    DSSU
      S1 = 10D+2Gp+2U, S2 = 12D+2Gp
  FR2 60 kHz:
    DDDSU
  FR2 120 kHz:
    DDDSU
    DSDSU
      S = 10D+2Gp+2U
TDD configurations for performance requirements can be different with initial alignment simulations assumption
Skip PDSCH scheduling for special sub-frames scheduling for initial simulation purpose, except for DSSU of 30 kHz, DSDSU of 120 kHz

## Slide 7: PDSCH demodulation tests (1/7)
Common test parameters
  For initial simulation alignment purpose: control symbols assumption: 2 symbols with full BW allocation for FR1, 1 symbol with full BW allocation for FR2
  Note: FFS for introducing performance requirements with partial BW PDCCH allocation

## Slide 8: PDSCH demodulation tests (2/7)
Number of Tx/Rx (For initial alignment simulation purpose)
  FR1:
    1 layer test: 2Tx 2Rx, 2Tx4Rx
    2 layer test: 2Tx 2Rx, 2Tx4Rx
    4 layer test: 4Tx4Rx,8Tx4Rx
    3 layer test: 4Tx4Rx
  FR2:
    1 layer test: 1Tx 2Rx
    2 layer test: 2Tx 2Rx
    4RX demodulation requirements in FR2 not excluded

## Slide 9: PDSCH demodulation tests (3/7)
Test metric
  At least for FR1: Reuse LTE metric as throughput vs. SNR
    Test point: 70% (normal demodulation test cases)
    FFS for other test point(s) of some specific test cases
  FFS for test metric for URLLC specific test cases if any
MCS
  At least covering below MCS levels:
  QPSK 1/3, 16QAM 1/2, 64QAM 3/4, 256QAM 4/5 (FR1 only)
HARQ parameters and RV sequence
  FDD: Max number HARQ transmission 4
  RV sequence for alignment simulation purpose:
    Option 1: {0, 1 ,2,3} for QPSK and 16QAM and {0,0,1,2} for 64QAM and 256QAM
    Option 2: {0, 2, 3,1} for all the modulation orders

## Slide 10: PDSCH demodulation tests (4/7)
PDSCH scheduling (For initial alignment simulation purpose):
  Full PRB allocation with channel bandwidth
  PDSCH mapping type: both type A and type B
  Further discussion for candidate options this week for PRB bundling size
    2
    FFS for the values of introducing performance requirements
  Random Precoding, per slot, per 2RBs (codebook configuration Single panel Type 1)
Note: FFS for test set-up for introducing PDSCH performance requirements

## Slide 11: PDSCH demodulation tests (5/7)
DMRS configuration
  Candidate options for defining performance requirements:
    Type 1 or 2, 1 symbol FL DMRS without additional symbol
    Type 1 or 2, 1 symbol FL DMRS 1 additional symbol
    Type 1 or 2, 1 symbol FL DMRS 2 additional symbol
  For initial alignment simulation purpose:
    Type 1, 1 symbol FL DMRS 1 additional symbol for FR1
    Type 2, 1 symbol FL DMRS 2 additional symbol for FR2
    Type 1, 1 symbol FL DMRS 1 additional symbol for FR2
  Note: Detailed test configurations for non-slot test cases if any in FR2 FFS

## Slide 12: PDSCH demodulation tests (6/7)
PTRS
  PTRS is configured when introducing performance requirements in FR2
  For initial simulation purpose:
    Using Phase noise model in TR 38.803 models for initial simulation purpose
    PTRS configuration (port 1, per 2PRB in frequency domain, per symbol in time domain)
TRS
  TRS configured when introducing performance requirements for both FR1 and FR2
  FFS for detailed configuration of TRS configuration
    Option 1 for information:
      FR1: periodicity 20 ms , power boosting [6dB], 2 slots
      FR2: periodicity 10 ms , power boosting [6dB], 2 slots
    Other options are not excluded

## Slide 13: PDSCH demodulation tests (7/7)
Reference Receiver (For initial alignment purpose):
  Rank1: MMSE-IRC/MMSE
  Layer 2,3,4: MMSE-IRC/MMSE and R-ML
  FFS for the receiver assumptions for performance requirements

## Slide 14: CSI tests
Overall Test Configuration & Scope
  First priority focused on:
    NZP CSI-RS for channel measurement CSI-IM for interference measurement
    CSI report types: periodic CSI report and aperiodic CSI report
    CSI-RS resources types: periodic and aperiodic
PMI reporting
  In Rel-15 focused on Type-I single panel codebook