## Slide 1: WF for dynamic transient period location for NR
Qualcomm, Ericsson, Vivo, Intel, Huawei
3GPP TSG-RAN4 Meeting #87
Busan, South Korea, 21 - 25 May 2018
R4-1808112

## Slide 2: Background PRACH RAN1 Agreement in 92bis meeting
UE does not simultaneously transmit PRACH and PUSCH/PUCCH/SRS in, at least, single CC and in intra-band CA, during any of the following scenarios:
  Same slot
  When the gap between the end of PRACH (PUSCH/PUCCH/SRS) and the start of PUSCH/PUCCH/SRS (PRACH) is less than N symbols
    N = 2 for 15 kHz and 30 kHz SCS.
    N = 4 for 60 kHz and 120 kHz SCS.
Working assumption: Reference SCS for determining N is the SCS for UL BWP.
FFS: inter-band CA.
Transmission of PRACH or SR (on PUCCH) if any, is up to UE implementation.

## Slide 3: Clarification of current agreement
The current mask is unclear, especially, for highest SCS with short length of symbol.
Intel would like to clarify and have a separate diagram like SRS case
Figure 6.3.3.7-1: PUCCH/PUSCH/SRS time mask when there is a transmission before or after or both before and after SRS

## Slide 4: Basic rules -2
Each channel on either side of the transient shall be characterized by its length (without any transient period)
Priority:
  Short > Long for a given channel
FFS: [In intra-band CA, the rules for the carrier with short length channel previal over those of the other CCs.]
FFS: RB hopping should also be studied.
Label | # of symbols
Short | < 3
Long | ≥3

## Slide 5: Basic Rules -4
Option 1:
  Provide for a GAP between symbols with power change when transient period even on one side.
Option 2 :
  Leave it for implementation on UE and gNB
  Allow for opportunistic recovery of the symbols
Option 2A :
  Introduce UE capability on UE transient parameter
  Leave it for implementation on UE and gNB
  Allow for opportunistic recovery of the symbols
Option 3:
  Allow for a GAP when the transient is on both sides of a symbol
  When the transient period is only on one side then no GAP is allowed
High SCS cases: GAP or not?

## Slide 6: Basic Rules -5
The number of power changes per slot adds burden on UE SW programming. Hence limiting the max number of power changes per slot is preferred.
Option 1:
  Limit the number of power changes:
    For FR1, FR2 to at least every ‘x’ symbols. Ex: x=2/3 [per physical channel]
  Send LS to RAN1
Option 2:
  Limit the number of power changes per slot
  Send LS to RAN1
Option 3:
  Don’t limit the number of power changes per slot
Companies are encouraged to submit proposals in the next meeting on this topic.
Power change frequency per slot

## Slide 7: Basic Rules -6
There could be cases where the next symbol is blanked during runtime
Proposal:
  Irrespective of the next symbol is blanked or not use the same rules to determine the location of the transient period
What if the next symbol is blanked?

## Slide 8: [One potential] logic to determine the location of transient period
If one of the channels is PRACH:
  Transient period shall be placed completely in the GAP before or after PRACH agreed by RAN1
Else if there a transient on both sides of a symbol (highest SCS)
  Blank that symbol (i.e. Don’t configure two consecutive power changes for UE)
Else if the transient is between short and long channels:
  Transient period is placed completely in the symbol belonging to the long channel
Else if both channels are short
  If the channel on the right of the transient has DMRS as the first symbol
    Transient period shall be placed completely Inside of DMRS
  Else
    Transient period shall be symmetrically shared

## Slide 9: Final format into 38.101
Figures will be added to 38.101 instead/along of rules

## Slide 10: OFF power requirement doesn’t apply when a symbol is blanked
The symbol duration is < On2Off +OFF2ON time