## Slide 1: 3GPP TSG RAN WG4 Meeting #87 R4-1808130 Busan, Korea, May 21st – 25th, 2018
WF on calibration gap
Qualcomm, Intel

## Slide 2: Background
Two types of gaps have been discussed
  Rank restricted gap (RRG)
  Total gap (TG)
In [4] it was concluded that network and UE must have knowledge of the TG location since UE can not even receive data in the slot designated as gap
[1] R4-1806329, On PA calibration gap, Intel Corporation
[2] R4-1807422, On calibration gap for FR2, Huawei
[3] R4-1807678, PA calibration gaps for FR2 UE’s, Nokia
[4] R4-1807881, Calibration gap configuration, Qualcomm
[5] R4-1807882, draftCR for 38.101-2 Calibration gap general section changes, Qualcomm
[6] R4-1807885, LS on calibration gap configuration, Qualcomm

## Slide 3: Way forward on calibration gap
UE is allowed periodically drop transmission on one TX if UE is configured only for 2Tx transmissions for not shorter than period of RRG (1 sec), probability should be considered further
  Up to1slot per second can be used for rank restricted based PA calibration
UE which declares the need for total calibration gap through capability, will be scheduled for a total gap (TG) periodically through RRC
  During the TG UE shall comply to the OFF power and other emission requirements
UE will be informed about the location of the TG with RRC signaling
LS to inform need for RRC signaling for TG will be sent to RAN2 in this meeting (RAN4#87)