## Slide 1: WF for simultaneous RxTx UE capability for NR
Ericsson, [ … ]
3GPP TSG-RAN4 Meeting #87
Busan, South Korea, 21 - 25 May 2018
R4-1808131

## Slide 2: Background: Three issues
Discussions on: “Simultaneous RxTx will not consider TDD-FDD cases, since this is assumed as supported for TDD-FDD”.
Discussions on: How to handle TDD-TDD cases?
Discussions on: “The criteria of mandating simultaneous RxTx, including which level MSD or which order of IMD/Harmonic interference is acceptable.”

## Slide 3: WF on “Simultaneous RxTx will not consider TDD-FDD cases, since this is assumed as supported for TDD-FDD”.
For LTE combinations with both UL for which this capability was supported, the same will be adopted in LTE-NR NSA combinations
  For other band combinations, the capability will be discussed on case by case basis
  Example Criteria: band combinations involving bands that are close to each other will be discussed on case-by-case basis; Example combinations: 7+38, 3+39, 7+40
  Other criteria are not precluded
Include this in the LS to RAN2: For TDD-FDD band combinations for which simultaneous RxTx capability is agreed to be supported, corresponding capability indication must be set to “supported”.

## Slide 4: WF on “How to handle TDD-TDD cases? “
CA_n39A-n78A
CA_n39A-n79A
CA_n39A-n41A
CA_n41A-n79A
DC_39A-n78A
DC_39A-n79A
DC_39A-n41A
DC_41A-n79A
DC_41A-n41A
DC_41A-n77A
DC_41A-n78A
DC_41A-n79A
DC_42A-n77A
DC_42A-n78A
DC_42A-n79A
CA_n41A_n78A
CA_n77A_n79A
CA_n78A_n79A
CA_n77A_n79A
CA_n78A_n79A
Green: Simultaneous TxRx will be supported
Crossed out: Simultaneous TxRx will be discussed case-by-case
Rest of cases: Simultaneous TxRx will be discussed case-by-case

## Slide 5: WF on TDD-TDD criteria
Isolation between the bands are the main criteria, need to be checked on case-by-case basis
  Example: 39+77 of sufficient isolation
  Example: 41+77- need to be checked