## Slide 1: UE RF requirements for PC5 in FR2
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea(Republic of), 21-25 May 2018
R4-1808140

## Slide 2: Background
UE RF requirements for PC4 for n257 were agreed as below [1].
PC5 is also proposed for narrower spherical use case such as FWA.
  PC5 is defined with max EIRP of 43 dBm and TRP of 23 dBm.
EIRP |  |  | EIS | TRP
Max | Min peak | 20%tile | Max peak | Max
43 dBm | 34 dBm | 25 dBm | -97 dBm/50MHz | 23 dBm
[1] R4-1808110, “FR2 Type 3 UE Power Class 4 RF Requirements”, NXP Semiconductors, Verizon

## Slide 3: Proposal
Specify UE RF requirements for PC5 for n257 as below in Rel-15.
The intention is to achieve higher peak EIRP with maintaining max EIRP and TRP of Handheld UE (i.e. 43 and 23 dBm) and avoid unnecessary requirements such as wide spherical performance.
EIRP |  |  | EIS | TRP
Max | Min peak | [95] %tile | Max peak | Max
43 dBm | [34] dBm | [31] dBm | [-97] dBm/50MHz | 23 dBm