## Slide 1: WF on Finalizing FWA (FR2 Power Class 1) Requirements
Samsung, Verizon, Intel, Qualcomm, NXP
R4-1808151
3GPP TSG-RAN WG4#87 Meeting
Busan, Korea (Republic of), May 21-25, 2018
Agenda: 7.5.7.1

## Slide 2
Way Forward (1)
Minimum peak EIRP for FR2 Power Class 1 (FWA UE Type with 55dBm EIRP limit, operating in stationary location) is defined as:
  40 dBm for 28GHz band;
  38 dBm for 39GHz band.
Spherical coverage requirement is defined as:
  85%-tile requirement for EIRP CDF is 32 dBm for 28GHz band;
  85%-tile requirement for EIRP CDF is 30 dBm for 39GHz band.
Minimum output power level:
  4dBm in terms of EIRP for minimum power level for FR2 Power Class 1.
Minimum peak EIS (Channel BW is 50MHz):
Other requirements should be specified in RAN4#87 to finalize all expected requirement.
 | 28GHz | 39GHz
Minimum Peak EIS | [-97.51] dBm | [-94.51] dBm

## Slide 3: Way Forward (2)
RF requirement for FR2 Power Class 1 (FWA UE type with 55dBm EIRP, operating in stationary location) should be finalized in RAN4 #87 based on the following understanding of expected RF requirement changes:
Section Name | Expected RF requirement changes for FWA UE type (max 55dBm EIRP, operating in stationary location)
Section 5.2 Operating Bands | No
Section 5.3 Channel bandwidth | No
Section 5.4 Channel arrangement | No
Section 6.2 Transmitter power | Yes - Power Class (minimum Peak EIRP) - Spherical coverage - MPR No ACLR need to be revisited
Section 6.3 Output power dynamic | Yes: - Minimum output power
Section 6.4 Transmit signal quality | Yes: - EVM condition needs to be revisit depending on minimum output power
Section 6.5 Output RF spectrum emissions | No
Section 7.2 Diversity characteristics | No
Section 7.3 Reference sensitivity power level | Yes - Peak EIS values
Section 7.4 Maximum input level | No
Section 7.5 Adjacent Channel Selectivity | No
Section 7.6 Blocking characteristics | No
Section 7.7 Spurious response | No
Section 7.9 Spurious emissions | No
Section 7.10 Receiver image | No

## Slide 4
References
Agenda | Tdoc number | Type/For | Title | Source
7.5.7.1 | R4-1806426 | Discussion/ Approval | Finalizing RF Requirements for FWA UE Type | Samsung
7.5.7.1 | R4-1806427 | Discussion/ Approval | Discussion on Spherical Coverage Requirement for FWA UE Type | Samsung
7.5.7.1 | R4-1806428 | Discussion/ Approval | UE minimum output power requirement for FWA UE Type | Samsung
7.5.7.1 | R4-1806573 | Discussion/ Approval | FR2 peak EIRP requirement for FWA | Intel Corporation
7.5.7.1 | R4-1806574 | Discussion/ Approval | FR2 peak EIS requirement for FWA | Intel Corporation
7.5.7.1 | R4-1807828 | Other/ Approval | Peak EIS of Type 4 UE | NXP Semiconductors Netherlands
7.5.7.1 | R4-1807849 | Other/ Approval | Peak EIRP of Type 4 UE | NXP Semiconductors Netherlands
7.5.7.1 | R4-1807890 | Other/ Approval | On FR2 Type 4 UE Performance Requirements | Qualcomm Incorporated
7.5.7.1 | R4-1807175 | Other/ Approval | Additional FWA requirements in FR2 | NTT DOCOMO, INC.
7.5.7.2 | R4-1806430 | Discussion/ Discussion | Handling UE Types in FR2 | Samsung
7.5.7.2 | R4-1806431 | LS out/ Approval | LS to RAN2 on UE Capability for mmWave UE Type | Samsung
7.5.7.1 | R4-1807887 | Other/ Approval | FWA Requirement Structure | Qualcomm Incorporated
7.5.7.1 | R4-1807889 | DraftCR/ Endorsement | draftCR for 38.101-2 FWA requirement skeleton | Qualcomm Incorporated