## Slide 1: 3GPP TSG-RAN WG4 RAN4-87 Busan, Korea, 21 - 25 May, 2018
Ericsson, Huawei, ZTE
Draft WF on Extension of Immunity Exclusion Bands for AAS-NR
R4-1808314

## Slide 2: Background
In [1], Ericsson presented a proposal to extend the exclusion bands for RI beyond the OOB limits (20 and 60 MHz) to ensure the levels used in EMC testing will not be stricter than the levels defined for blocking.
In the same document, Ericsson presented the methodology used by ETSI in the calculation of Exclusion Bands. According to ETSI EN 301 489 – 1 [2] in section 4.3, the exclusion bands shall be derived using the methodologies detailed in the clauses 4.3.2 (Transmitter) and 4.3.3 (Receiver). ETSI EN 301 489-50 [3] makes use of the methodology described in clause 4.3.3 in [2] to calculate the exclusion bands applicable for BS.
According to [2][3], the starting point for determining the size of the Exclusion Band is the channel bandwidth (ChWRx) or bandwidth of the receiver under test (BWRx) in ETSI standards.
The current definition of Exclusion Bands in [3] “is derived using the formula in clause 4.3.3.1 of ETSI EN 301 489-1 where the value of n is one” while BWRx/ChWRx=20MHz. This criterion has been reflected in the different 3GPP EMC specifications. Current scope of EN 301 489-50 includes technologies such as UTRA, E-UTRA, GSM, MSR where the Channel Bandwidth (ChWRx)operating band did not exceed the 20 MHz and there was not multiple carriers.
Ericsson affirms that even though the values n=1 and ChWRX =20 MHz has been applied in different 3GPP EMC specifications and in ETSI EN 301 489-50, both 3GPP and ETSI need to be updated since new BS solutions demand more bandwidth. In addition, new BS solutions can combine multiple carriers which has enabled a number of separate carriers enabling an increase in the peak user data rates and the overall capacity of the networks. exploiting fragmented spectrum allocations. Therefore, BWRx/ChWRx value should consider new technical considerations and the value of n should be defined considering the number of carriers supported by the BS.

## Slide 3: WF Agreement
The goal with the definition of exclusion bands is to protect the receiver from potential damage/undue stress during the test. Because of this, the exclusion band is directly linked to the technology employed by the EUT, the expected operating environment and the service the EUT is intended to deliver.
From EMC RI requirements point of view, use of wider operating bands, and/or CA, and/or wider NR channel bandwidths, may require wider Rx exclusion bands for both AAS NR and NR BS, which is subject to further study.
Increasing from 20 MHz to up to 60 MHz the exclusion band size (depending on the type of BS and the operating band) has reflected this need. However, a
New value of the Exclusion band size might be required considering the technology evolution.
The identified options are :
Option 1: Use the methodology proposed by ETSI in ETSI EN 301 489 – 1 [2] to calculate the size of the Rx exclusion band defined for AAS BS (OTA AAS BS and hybrid AAS BS) in TS 37.114 and for NR BS (types 1-C, 1-H, 1-O and 2-O) in TS 38.113.
  Consider aligning terminology used by ETSI with 3GPP TS terminology.
  Clarifying the use of Channelized/Non-channelized approach.
  Parametrization for wider receiver exclusion bands calculation.
Option 2: Keep it the same as defined in TS 38.113 and TS 37.114 for Rel-15.
Option 3: Other solutions not precluded.

## Slide 4: References
[1] R4-1806969.Definition of Receiver Exclusion Bands for AAS and NR. Ericsson. RAN4#87.
[2] ETSI EN 301 489 – 1. ElectroMagnetic Compatibility (EMC) standard for radio equipment and services; Part 1: Common technical requirements; Harmonised Standard covering the essential requirements of article 3.1(b) of Directive 2014/53/EU and the essential requirements of article 6 of Directive 2014/30/EU.
[3] ETSI EN 301 489 – 50. ElectroMagnetic Compatibility (EMC) standard for radio equipment and services; Part 50: Specific conditions for Cellular Communication Base Station (BS), repeater and ancillary equipment; Harmonised Standard covering the essential requirements of article 3.1(b) of the Directive 2014/53/EU-