## Slide 1: WF on NR test configuration
ZTE, Nokia, Huawei, Ericsson
3GPP TSG-RAN WG4 #87 R4-1808317
Busan, Korea, 21st -25th May, 2018

## Slide 2: Background(1)
In RAN4#86bis [1] , five test configurations should be defined for NR BS conformance testing
  NRTC1: NR contiguous spectrum operation
  NRTC2: Contiguous CA occupied bandwidth
  NRTC3: NR non-contiguous spectrum operation
  NRTC4: NR multi-band test configuration for full carrier allocation
  NRTC5: NR multi-band test configuration with high PSD per carrier
For the TC generation,
  Test configuration generation for E-UTRA can be a starting point for NR conformance testing.
  Declared maximum Base Station RF Bandwidth should be used.
[1] R4-1805872, WF on Test configuration for NR BS conformance testing, Huawei, Ericsson, Nokia

## Slide 3: Background(2)
In RAN4#87, serveral contributions discussed the NR test configuration:
  R4-1806737 Test Configurations for NR only, Ericsson
  R4-1806778 On NR BS test configuration, ZTE Corporation
  R4-1807528 Test configuration for NR, Huawei, HiSilicon
  R4-1807529 Test cases for NR,Huawei, HiSilicon
  R4-1807873 On NR test configurations, Nokia, Nokia Shanghai Bell
  R4-1806779 TP to TS 38.141-1: Test configuration(Sections 4.7), ZTE Corporation

## Slide 4: WF on test configuration
For the NRTCx(i.e. NRTC 1~5) generation, the test signal used to build the test configuration should be:
  A typical channel BW with the smallest supported SCS.
  If this typical channel BW is not supported by the BS, the narrowest supported channel BW shall be selected instead.
  Typical channel BW is FFS. Some initial proposals are:
      For FR1 operating bands:
        5 MHz for bands less than 100MHz.
        20 MHz for bands larger than or equal to 100MHz.
      For FR2 operating bands:
        50 MHz and/or 100 MHz.
Other test signal for test configuration should not be precluded.