## Slide 1: WF on test models for NR conformance test
Nokia, Nokia Shanghai Bell, …
R4-1808320
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea, 21 - 25 May 2018
Agenda Item: 7.8.2

## Slide 2: Background (1/2)
During RAN4#87 meeting test models were discussed in the following contributions:
[1] R4-1808319 Test models for NR base station conformance testing, Huawei Telecommunication India, HiSilicon
[2] R4-1807872 NR Test models, Nokia, Nokia Shanghai Bell
This document summarizes the way forward on test models for NR conformance test

## Slide 3: Background (2/2)
Following E-UTRA test models are used in 36.141 specification:
E-UTRA test models (36.141): | This model shall be used for tests on:
E-UTRA Test Model 1.1 (E-TM1.1) | BS output power - Unwanted emissions - Occupied bandwidth, ACLR, Operating band unwanted emissions, Transmitter spurious emissions - Transmitter intermodulation - RS absolute accuracy
E-UTRA Test Model 1.2 (E-TM1.2) | Unwanted emissions - Occupied bandwidth, ACLR, Operating band Unwanted emissions
E-UTRA Test Model 2 (E-TM2) | Total power dynamic range (lower OFDM symbol power limit at min power), - EVM of single 64QAM PRB allocation (at min power) - Frequency error (at min power)
E-UTRA Test Model 2a (E-TM2a) | Total power dynamic range (lower OFDM symbol power limit at min power), - EVM of single 256QAM PRB allocation (at min power) - Frequency error (at min power)
E-UTRA Test Model 3.1 (E-TM3.1) | Output power dynamics - Total power dynamic range (upper OFDM symbol power limit at max power with all 64QAM PRBs allocated) Transmitted signal quality - Frequency error, EVM for 64QAM modulation (at max power)
E-UTRA Test Model 3.1a (E-TM3.1a) | Output power dynamics - Total power dynamic range (upper OFDM symbol power limit at max power with all 256QAM PRBs allocated) Transmitted signal quality - Frequency error, EVM for 256QAM modulation (at max power)
E-UTRA Test Model 3.2 (E-TM3.2) | Transmitted signal quality - Frequency error, EVM for 16QAM modulation
E-UTRA Test Model 3.3 (E-TM3.3) | Transmitted signal quality - Frequency error, EVM for QPSK modulation

## Slide 4: Way forward
Each of NR test model consist of following elements:
  Core requirements list for which given test model is used,
  Physical channel parameters of test model,
  Most of TMs include tables of specific parameters that are used for test models (eg. boosters PRBs, allocated PRBs etc. for both FDD and TDD).
Companies are encourage to further study if all TM that are used in E-UTRA test specification are needed for NR.
E-UTRA Physical channel parameters used in TMs should be reviewed and updated for NR.
Companies are encourage to further study which aspects of the NR PHY design and channels parameters are needed for TM design.
For each TM specific list of parameters should be create. There may be different list of parameters for each frequency range.
Efficient way to introduce list of parameters for TM (eg. boosted PRBs and allocated PRBs for given test models) should be consider.
For NR TDD operation configuration of TDD gNB needs to be decided to define test models.
Companies are encouraged to further study the test for mixed numerologies and decide further if we need the mixed numerologies tests.