## Slide 1: 3GPP TSG-RAN WG4 Meeting #87 Busan, Korea(Republic of), 21 - 25 May 2018
Huawei, Ericsson, Samsung
Way forward on BS FeNB-IoT demodulation performance
R4-1808448

## Slide 2: FeNB-IoT FDD part
  Use the similar simulation assumptions as preamble 0 and 1 defined for NB-IoT Release 13 for preamble format 2:
  For details, please refer to the next slide.
Number of TX antennas | Number of RX antennas | Repetition number | Propagation conditions and correlation matrix (Annex B) | Frequency offset | SNR[dB] |  | 
 |  |  |  |  | Preamble format 0 | Preamble format 1 | Preamble format 2
1 | 2 | 8 | AWGN | 0 | -2.1 | -2.1 | TBD
 |  |  | EPA1 Low | 200 Hz | 6.1 | 6.1 | TBD
 |  | 32 | AWGN | 0 | -6.8 | -6.8 | TBD
 |  |  | EPA1 Low | 200 Hz | 0.5 | 0.5 | TBD

## Slide 3: FeNB-IoT FDD part
Parameter | Values
NPRACH preamble format | 2
Number of Repetitions | 8, 32
Number of Subcarriers | 12
Antenna configuration | 1 x 2
Narrowband physical layer cell identity | 0
NPRACH signature | 0
frequency offset | 0Hz (AWGN); 200Hz EPA1
Propagation channels | AWGN, EPA1
Detection performance | Missed detection rate (1%) with false alarm rate (0.1%)
Timing estimation | Timing error probability with the limit of 3.646us
Timing Offset | T_CP/2

## Slide 4: FeNB-IoT TDD part
  Use the similar simulation assumptions as NPRACH FDD for NPRACH TDD for different preamble formats:
  FFS how to reduce the number of test cases.
Number of TX antennas | Number of RX antennas | Repetition number | Propagation conditions and correlation matrix (Annex B) | Frequency offset | SNR[dB] |  |  |  | 
 |  |  |  |  | Preamble format 0 | Preamble format 1 | Preamble format 2 | Preamble format 3 | Preamble format 4
1 | 2 | 8 | AWGN | 0 | TBD | TBD | TBD | TBD | TBD
 |  |  | EPA1 Low | [200 ]Hz | TBD | TBD | TBD | TBD | TBD
 |  | 32 | AWGN | 0 | TBD | TBD | TBD | TBD | TBD
 |  |  | EPA1 Low | [200] Hz | TBD | TBD | TBD | TBD | TBD