## Slide 1: Way-Forward on FR2 OTA unwanted emissions
Agenda Item: 7.7.2.5.2.3
Document for: Approval
Source: Ericsson, Nokia, Nokia Shanghai Bell, NTT DOCOMO, ZTE
3GPP TSG-RAN WG4 #87 Tdoc R4-1808504
Busan, Korea, 21 – 25 May 2018

## Slide 2: Off-line discussion points
Proposed FR2 mask levels in relation to the limits used in ITU-R sharing studies
  Conclusion that all proposals submitted align with those limits
Status of Category B spurious limits in Europe
Way-Forward agreements:
  OBUE border to spurious
  Mask levels & PTx threshold
  Clarification of Prated,t,TRP definition

## Slide 3: OBUE border to spurious
WAY-FORWARD:
The FR2 mask will be an OBUE mask (band centric).
The mask will extend to ΔfOBUE = 1.5 GHz outside the band

## Slide 4: Mask levels & PTx threshold
WAY-FORWARD:
Emission mask for 24.25 – 33.4 GHz (PTx threshold 30 dBm)
Emission mask for 37 – 52.6 GHz (PTx threshold 28 dBm)
Frequency offset from “edge of transmission” Δf | Limit | Measurement bandwidth
0  f < 0.1*BWcontiguous | Min(-5 dBm, Max(PTx – 35 dB, -12 dBm)) | 1 MHz
0.1*BWcontiguous  f < Δfmax | Min(-13 dBm, Max(PTx – 43 dB, -20 dBm)) | 1 MHz
Frequency offset from “edge of transmission” Δf | Limit | Measurement bandwidth
0  f < 0.1*BWcontiguous | Min(-5 dBm, Max(PTx – 33 dB, -12 dBm)) | 1 MHz
0.1*BWcontiguous  f < Δfmax | Min(-13 dBm, Max(PTx – 41 dB, -20 dBm)) | 1 MHz

## Slide 5: Prated,t,TRP definition
Prated,t,TRP = Rated total TRP output power declared per RIB
rated total TRP output power: mean power level declared by the manufacturer, that the manufacturer has declared to be available at the RIB during the transmitter ON period
WAY-FORWARD:
Consensus that “Total” means both polarizations and includes all sub-blocks in case of non-contiguous operation

## Slide 6: REFERENCES
R4-1806401, "Requirement on FR2 BS OTA out of band emission" (Samsung).
R4-1806929, "Further discussion on FR2 SEM" (ZTE).
R4-1806940, "BS Emission mask for FR2" (Ericsson, Nokia, Nokia Shanghai Bell).
R4-1807526, "Further consideration on FR2 SEM" (Huawei, HiSilicon).
R4-1807577, "SEM for FR2 NR BS" (NTT DOCOMO, INC.).