## Slide 1: Way Forward for impact analysis on Bluetooth and IEEE 802.11 operation for the new TDD E-UTRA band proposed by GlobalStar
CableLabs, Broadcom
08/24/2018
R4-1811569
3GPP TSG RAN4 meeting #88
Gothenburg, Sweden, August 20-24, 2018

## Slide 2: Background
GlobalStar received an allocation for TLPS in 2.4 GHz band by FCC subject to the certain restrictions (FCC 16-181).
Consequently, a work item for a new TDD E-UTRA band was approved in RAN #79 (RP-180583).
The work items includes a study phase with the following core objectives
  Define impact on 2.4 GHz Bluetooth operations
  Define impact on 2.4 GHz 802.11 operations
  Address potential BT, BLE and Wi-Fi coexistence issues

## Slide 3: Way Forward
Analyze on the impact of the 2483.5-2495 MHz band upon the ISM band WLAN and BT traffic:
  The impact on the highest BT channel (2480 MHz), concerning a low level hearing aid device (long life battery life, EIRP = 2.5 nW), located at 1 and 10 m away of a GlobalStar eNB (peak EIRP = 36 dBm)
  The impact on a channel 11 STA under two scenarios:
    located at equal distance of a channel 11 AP (EIRP = 23 dBm) and a GlobalStar eNB (EIRP = 36 dBm and a max conducted power spectral density limit of 8 dBm/3 kHz)
    located at distance d of a channel 11 AP (EIRP = 23 dBm) and at distance 0.1d of a GlobalStar eNB (EIRP = 36 dBm and a max conducted power spectral density limit of 8 dBm/3 kHz)
  The same impact analysis upon an AP under two scenarios:
    co-located at equal distance between a STA (EIRP = 17 dBm), operating on channel 11 and a eNB operating on a 2483.5 MHz channel edge (AP EIRP = 36 dBm, PSD=8dBm/3kHz).
    co-located at distance d of a STA (EIRP = 17 dBm), operating on channel 11 and at distance 0.1d of a eNB operating on a 2483.5 MHz channel edge (AP EIRP = 36 dBm, PSD=8dBm/3kHz).
2. GlobalStar shall present the results of their self-assessment comprising graphical information on the average co-existence traffic throughput, as a result of distance between WLAN STA/AP and BT (<2483.5 MHz) vs. the LTE eNB.
3. GlobalStar shall evaluate IDC impact when a LTE TDD UE operating in the 2483.5-2495 MHz is collocated with a BT/BLE/WiFi device.
4. The SI will get completed once the above targets will be achieved.

## Slide 4: Specifics of ISM Band Usage in U.S.
Channels 12, 13 and 14 are not allowed for Wi-Fi usage
Channels 12 and 13 are still used for Bluetooth
Guard band between the highest BT channel and the lower edge of the proposed E-UTRA band is 3.5 GHz only
Hearing aid devices with long-life batteries may use 2.5 nW (-26 dBm) EIRP while the max. eNB EIRP is 36 dBm; related power difference is 62 dB