## Slide 1: Way forward on applicability for gap pattern configuration
CMCC
3GPP TSG-RAN WG4 Meeting RAN4#88 R4-1811740
Gotherburg ,Sweden, 20 -24 Aug, 2018

## Slide 2: Background
According to the current applicability for gap pattern configuration, only gap pattern 0~3 can be configured if the measurement purpose includes E-UTRAN.
In RAN4#87 meeting, LS to RAN2 on measurement gap applicability (R4-1807971) was approved.
  RAN4 respectfully asks RAN2 to confirm if RAN2 has specified the capability indication signaling of supporting or not supporting short measurement gap (pattern #2 and #3) in NR standalone operation for LTE measurement, and if this signaling hasn’t been specified, RAN4 respectfully ask RAN2 to specify it in R15 specification.

## Slide 3: Background
UE not supporting short measurement gap can only perform measurement within 6ms MGL, e.g. gap pattern 0, 1, 4, 5.
UE supporting short measurement gap pattern#2 and #3 is capable of performing measurement within 3ms/4ms MGL, e.g. gap pattern 6~11.
Gap Pattern Id | Measurement Gap Length (MGL, ms) | Measurement Gap Repetition Period (MGRP, ms)
0 | 6 | 40
1 | 6 | 80
2 | 3 | 40
3 | 3 | 80
4 | 6 | 20
5 | 6 | 160
6 | 4 | 20
7 | 4 | 40
8 | 4 | 80
9 | 4 | 160
10 | 3 | 20
11 | 3 | 160
12 | 5.5 | 20
13 | 5.5 | 40
14 | 5.5 | 80
15 | 5.5 | 160
16 | 3.5 | 20
17 | 3.5 | 40
18 | 3.5 | 80
19 | 3.5 | 160
20 | 1.5 | 20
21 | 1.5 | 40
22 | 1.5 | 80
23 | 1.5 | 160

## Slide 4: Background
Proposed revision on the applicability for gap pattern configuration in R4-1810291 (CMCC):
  Apply gap pattern 0~11 to the case that E-UTRA measurement purpose in included.
  For EN-DC，the gap pattern 2, 3 and 6~11 are supported by UEs which support shortMeasurementGap-r14
  For SA, the gap pattern 2, 3 and 6~11 are supported only by the UEs which have a corresponding capability of short measurement gap

## Slide 5: Way forward
  Discuss whether and how to apply additional gap patterns (other than pattern 0~3) to E-UTRA measurement purpose in REL-15 TEI.
    If these additional gap patterns are agreed to be applied,
      Discuss on whether new UE capability is needed or existing signaling can be reused for those gap patterns
      Discuss whether to introduce new E-UTRA measurement requirements based on the potential new gap patterns in REL-15 TEI.