## Slide 1: Way forward on UE behavior before or after measurement gap
ZTE, …
3GPP TSG-RAN WG4 Meeting #88
Gothenburg, Sweden, 20 - 24 August, 2018
R4-1811869

## Slide 2: Background
In previous WF R4-1809406
  RAN4 try to define deterministic UE behavior for UL transmission after measurement gap, i.e. define UE behavior in the way such that network knows whether UE will transmit or not under certain conditions.
  Following aspects should be considered when defining the UE behavior:
    UE measurement time and re-tuning time if UE transmits UL after gap
    NR measurement being based on SMTC window
    MGTA (measurement gap timing advance) in NR
    Flexible UL/DL assignment of symbols in NR
    NR symbol length depending on SCS
    UL-DL and DL-UL switching time in NR

## Slide 3: Background
Agreements in the RAN4#88 meeting
  When only MGTA or both MGTA and TA applies to measurement gap at UE in addition to measurement gap offset, the following UE behavior in the slot immediately before/after measurement gap should be specified for NR TDD.
    UE is required to conduct reception of DL data in the slot occurring immediately before the measurement gap if the last DL symbol in the slot is not overlapped with the measurement gap.
    UE shall transmit UL data in the slot occurring immediately before the measurement gap if the last UL symbol in the slot is not overlapped with the measurement gap.
    UE shall transmit UL data in the slot occurring immediately after the measurement gap if the first UL symbol in the slot is not overlapped with the measurement gap.

## Slide 4: Slots before and after measurement gap
  When MGTA is NOT applied,
    the slot before the measurement gap is slot j, 2j+1, 4j+3 and 8j+7 for 15kHz, 30kHz, 60kHz and 120kHz respetivley
    the slot after the measurement gap is slot j+N+1, 2(j+N+1), 4(j+N+1), 8(j+N+1) for 15kHz, 30kHz, 60kHz and 120kHz respetivley.

## Slide 5: Slots before and after measurement gap
  When MGTA is applied,
    the slot before the measurement gap is slot j-1, 2j, 4j+1 and 8j+3 for 15kHz, 30kHz, 60kHz and 120kHz respetivley
    the slot after the measurement gap is slot (j+N)+1, 2(j+N)+1, 4(j+N)+2, 8(j+N)+4 for 15kHz, 30kHz, 60kHz and 120kHz respetivley.
  Note1: The figure dipects serving cells with different SCSs.
  Note 2: Interruption requirements also needs to be taken into accout.

## Slide 6: Definition of starting point of MG
For EN-DC (LTE is the master cell, NR cells are not in MCG)
  If per-UE MG is configured,If per-UE measurement gap is configured with MG timing advance of 0ms, a measurement gap starts at the end of the latest LTE subframe occurring immediately before the measurement gap among MCG serving cells subframes.
  If per-FR measurenet gap for FR1 is configured with MG timing advance of 0ms, this measurement gap for FR1 starts at the end of the latest LTE subframe occurring immediately before the measurement gap among MCG serving cells subframes in FR1.
  If per-FR measurenet gap for FR2 is configured with MG timing advance of 0ms, this measurement gap for FR2 starts at [FFS].
FFS for SA
FFS when MGTA of 0.5ms or 0.25ms is applied for EN-DC and SA.

## Slide 7: UE behavior before and after measurement gap
UE behaviour before and after measurement gap should be considered for following scenarios
  When MGTA (0.5ms for FR1 and 0.25ms for FR2) is applied
    NR TDD
    NR FDD
    NR CA
      Different SCSs on different SCells
  When MGTA (0.5ms for FR1 and 0.25ms for FR2) is NOT applied
    NR TDD
    NR FDD
    NR CA
      Different SCSs on different SCells
  Note: interruption requirements for measurement gap should also be taken into account.

## Slide 8: WF
Companies are encouraged to bring further analysis in RAN4#88bis meeting.

## Slide 9: Reference contributions
R4-1810742, Discussion on UL transmission after measurement gap, ZTE
R4-1810220, Discussion on UE behavior in the slot immediately before/after measurement gap, LGE
R4-1810212, CR on starting point to execute the measurement gap, Intel Corporation