## Slide 1: 3GPP TSG-RAN WG4 Meeting #88bis Chengdu, China, 8 – 12 October 2018
Huawei, HiSilicon
Way forward on FR2 RRM test
R4-1813001

## Slide 2: Background
  For FR2 RRM tests, the AoA, SNR/SINR side condition and the definition of ideal measurement are open.
  The WF from Testability SI in RAN4#88 on FR2 RRM testing is captured in R4-1811890
  It is agreed in RP-182149
For FR2, only the RRM test cases with the single AoA test setup will be discussed in Q4 2018 The test cases with the two AoA test setup will be deferred after December to Q1 2019

## Slide 3: Way forward
  Below principle are adopted for determining AoA in FR2 RRM test cases in Q4/18
    For RRM test cases involving two cells, RAN4 should develop FR2 test cases with single AoA in Q4/18.
      The development and applicability of these test cases with two AoA could be discussed in Q1/19.
    Serving cell and target cell are both transmitted from the Rx beam peak direction.
    UE rotation is not considered in the FR2 RRM test

## Slide 4: Way forward
  For cases where serving and target cell are on the same frequency in the test, the methodology in setting the power and noise is
    Wanted noise is transmitted from the serving cell only
    Wanted noise is set to give 1dB difference between Reference point SNR and Baseband SNR for the serving cell and the target cell, using the same UE parameters as in R4-1811892.
    This gives Noc level -153dBm/Hz for wanted noise

## Slide 5: Way forward
  For test cases verifying the absolute measurement accuracy, the ideal measurement result is determined based on
    The ideal measurement result at the reference point assuming omni directional with 0dBi antenna gain
    The limits on the maximum and minimum effective antenna gain in the UE Rx beam peak direction
      This includes the effective array gain and total implementation loss
  Companies are encouraged to provide inputs on the maximum and minimum effective antenna gain in the UE Rx beam peak direction