## Slide 1: WF: Summary of proposals for TDL channel models
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #88-bis R1-1813734
Chengdu, China, 8 – 12 October 2018
Agenda item: 7.13.1.5

## Slide 2: References
Huawei contribution R4-1812326 ”Simplification of FR1 TDL channel models”
Intel contribution R4-1812177 ”Discussion on simplified TDL channel models”
Keysight contribution R4-1813572 ”Impact of tap reduction on TDL models”
Ericsson contribution R4-1812853 ”Simplified propagation channel models for FR1 UE demodulation requirements”

## Slide 3: Power cutting vs decimation
Original
Power cut
Final
Original
Sparse
Final

## Slide 4: TDL-A
Huawei
Intel
Keysight
Ericsson

## Slide 5: TDL-B
Huawei
Intel
Ericsson
Keysight

## Slide 6: TDL-C
Huawei
Intel
Keysight
Ericsson

## Slide 7: Numerical Comparison
Model | Company | Number of Taps | Delay Spread [ns] | Maximum Excess Delay [ns]
TDL-A | Reference | 23 | 30.0 | 290
 | Huawei | 12 | 30.0 | 225
 | Intel | 7 | 30.3 | 150
 | Keysight | 12 | 30.0 | ~140*
 | Ericsson | 12 | 29.5 | 165
TDL-B | Reference | 23 | 100.0 | 480
 | Huawei | 12 | 100.0 | 440
 | Intel | 11 | 99.5 | 310
 | Keysight | 12 | 100.4 | ~310/490 (method 1/2)*
 | Ericsson | 12 | 99.7 | 335
TDL-C | Reference | 24 | 300.0 | 2595
 | Huawei | 12 | 300.0 | 2235
 | Intel | 11 | 300.8 | 1155
 | Keysight | 12 | 299.8 | ~1200*
 | Ericsson | 11 | 300.0 | 1535
*Approximate value from the graphics

## Slide 8: Observations
Observation 1: All proposals meet the requirement on maximum number of taps (12)
Observation 2: It is difficult to compare the frequency correlation functions. However, some of them meet <0.6 correlation better than others.
Observation 3: weak tap cutting leads to shorter maximum excess delay.

## Slide 9: Proposal
Proposal: The selection of the TDL model is based on FCF, rms delay spread, and the maximum excess delay.